## Slide 1: Computer networking
Olivier Bonaventure
http://perso.uclouvain.be/olivier.bonaventure

## Slide 2: Teaching material
Third edition https://www.computer-networking.info
Feedback/Fixes/Suggestions/Comments
  http://github.com/cnp3/ebook

## Slide 3: Networking blog
https://blog.computer-networking.info

## Slide 5: Question
What are the topics that you expect to learn during this course ?

## Slide 6: A simple Internet
R3
R1
RA
RB
RY
RX
RN
RM
R2

## Slide 7: Course structure
Part 1 : Host behavior
  Principles: serving applications, security, reliable transfer
  Protocols: HTTP, SMTP, DNS, TLS, TCP, UDP,…
Part 2 : Building a network
  Principles: packet forwarding, routing, congestion control
  Protocols: IPv6, MPLS, RIP, OSPF, BGP, Ethernet, Wi-Fi
Practice
  Learning by doing

## Slide 8: Course organisation
First pass on the week topic (Thursday)
Students read book and prepare exercises
  Inginious questions
  Multiple choice questions
    Some weeks : practical exercises as well
Discussion with teaching assistants (Thu/Fri)
Second pass on the week topics (Thursday)

## Slide 9: Course evaluation
Projects (35%)
  Analyze a networked app (20%)
  Network configuration project (15%)
Written Exam
  Both exercises and theory (65%)
Bonus

## Slide 10
https://moodle.uclouvain.be/mod/choice/view.php?id=48329

## Slide 11: Learning by doing ?

## Slide 12: We also have tools

## Slide 13: A simple Internet
R3
R1
RA
RB
RY
RX
RN
RM
R2
Internet

## Slide 14: Question
During this course, we will describe all the components of the Internet, but when was this network created?

## Slide 15: ARPANet
First ARPANet message, Oct. 29, 1969 https://en.wikipedia.org/wiki/ARPANET

## Slide 16: Connecting two hosts

## Slide 17: Question
What are the technologies that allow to connect two computers together ?

## Slide 18: Question
What is the bandwidth (in bits/sec) that you can achieve on a telephone line over a several kilometers ?

## Slide 19: VDSL and G.Fast
https://techzine.alcatel-lucent.com/fixed-access-stay-ahead-ultra-broadband-curve

## Slide 20: Question
What is the bandwidth (in Mbps) that you can achieve using current wireless (4G/5G, Wi-Fi) networks ?

## Slide 21: Question
What is the bandwidth (in Gbps/sec) that you can achieve on an optical fiber ?

## Slide 22: Optical fiber
http://www.nature.com/nphoton/journal/v7/n5/fig_tab/nphoton.2013.94_F1.html

## Slide 23: Question
What is the minimum delay (in msec) required to transmit one byte from Louvain-la-Neuve to Barcelone (+-1000 km) ?

## Slide 24: Modems and ISDN
Notes: Morse telegraph - 1940
110 Bps AT&T 1950
300 BPs AT&T http://www.history-computer.com/ModernComputer/Basis/modem.html
1988 : Robotics 9600 bps https://en.wikipedia.org/wiki/File:Fax_modem_antigo.jpg
Minitel : années 1980

## Slide 25: Local area networks

## Slide 26: xDSL and DOCSIS

## Slide 27: WiFi
802.11
802.11b
802.11a
802.11g
802.11n
802.11ac

## Slide 28: Cellular networks
2G
  14.4 Kbps, GPRS: 56.6 Kbps, EDGE: 236 Kbps
3G
  2, 3, 14 Mbps
4G
  HSPA: 14, 42 Mbps, LTE : 173, 326 Mbps
https://en.wikipedia.org/wiki/List_of_device_bit_rates
http://www.netmanias.com/en/post/korea_ict_news/7591/korea-lte-mp-tcp-wi-fi/kt-s-giga-lte-world-s-first-commercial-wireless-1-giga-3-band-ca-giga-wifi

## Slide 29: The physical layer
Transmitting bits over a wire
Time sequence diagram

## Slide 30: Question
What are the types of errors that can affect the transmission of bits on a wire or radio link ?
  Bit error, 0 replaced by 1 (and reverse)
  Creation of bits (receiver receives more bits than those sent by sender)
  Loss of bits (receiver receives fewer bits than those sent by sender)

## Slide 31: The physical layer service
  unreliable service
    transmission errors
Physical layer
Physical layer
Physical transmission medium
Bits
010100010100010101001010

## Slide 32: Time sequence diagram
How to represent the operation of the physical layer ?
A B
Data.request(0)
0
Data.ind(0)
Data.request(1)
Data.ind(1)
Data.request(1)
Data.ind(1)
1
1

## Slide 33: Time sequence diagram
How to represent the unreliablity of the physical layer ?
A B
Data.request(0)
0
Data.ind(0)
Data.request(1)
Data.ind(0)
Data.request(1)
Data.ind(1)
0
1

## Slide 34: Time sequence diagram
How to represent the fact that the physical layer can loose bits ?
A B
Data.request(0)
0
Data.ind(0)
Data.request(1)
Data.request(1)
Data.ind(1)
1

## Slide 35: Time sequence diagram
How to represent the fact that the physical layer can create bits ?
A B
Data.request(0)
0
Data.ind(0)
Data.request(1)
Data.ind(1)
1
Data.ind(1)
Data.request(0)
0
Data.ind(0)

## Slide 36: How do Internet hosts exchange data ?
Principles
  Each host is identified by a unique IP address
  Hosts echange data inside packets containing
    IP address of the source
    IP address of the destination
    Data

## Slide 37: Length of IP address
What is the length of an IP address in bits ?

## Slide 38: Internet Protocol (IP) addresses
IPv4
  32 bits, written as a.b.c.d, e.g. 130.104.1.1
IPv6
  128 bits, written in hexadecimal notation,
    2001:06a8:3080:0001:0000:0000:0000:0003
    2001:6a8:3080:1::3

## Slide 39: IPv6 addresses
Each IPv6 address is encoded in 128 bits
  3.4 x 10^38 possible addressable devices
    6.65 x 10^23 addresses per square meter
Why 128 bits ?
IPv4
IP version 6
Notes: IP version 4 supports 4,294,967,296 distinct addresses, but some are reserved for :
private addresses (RFC1918)
loopback (127.0.0.1)
multicast
...

## Slide 40: IPv6 adoption
What is percentage of IPv6 users in Belgium ?
Feb. 2025: 63.2%

## Slide 41: Textual representation
  Hexadecimal format
    FEDC:BA98:7654:3210:FEDC:BA98:7654:3210
    1080:0:0:0:8:800:200C:417A
  Compact hexadecimal format
    Some IPv6 addresses contain lots of zero
      use "::" for one or more groups of 16 zeros.
        1080:0:0:0:8:800:200C:417A = 1080::8:800:200C:417A
        FF01:0:0:0:0:0:0:101 = FF01::101
        0:0:0:0:0:0:0:1 = ::1

## Slide 42: Types of interactions between two hosts
Datagram
  Source sends a message to destination
    Restriction on message length
Bytestream (aka Unix pipe)
  All the bytes sent by the source in the bytestream will be later received by destination

## Slide 43: Datagram exchange
A B
Data.request(Hello,)
Data.ind(Hello,)
Data.request(Bob)
Data.request(!)
Data.ind(!)
Data.ind(Bob)
Data.req(Nice to meet you)
Data.ind(Nice to meet you)

## Slide 44: Limitations of datagrams
Message length
  In theory 64 KBytes
  In practice more than 1400 bytes is often risky
Datagram sequence is not always preserved
Datagrams can be lost
Datagrams can be duplicated

## Slide 45: Lost datagrams
A B
Data.request(Hello,)
Data.ind(Hello,)
Data.request(Bob)
Data.request(!)
Data.ind(!)
Data.req(Nice to meet you)

## Slide 46: Out-of-sequence Datagrams
A B
Data.request(Hello,)
Data.ind(Hello,)
Data.request(Bob)
Data.request(!)
Data.ind(!)
Data.ind(Bob)
Data.req(Nice to meet you)
Data.ind(Nice to meet you)

## Slide 47: Duplicated Datagrams
A B
Data.request(Hello,)
Data.ind(Hello,)
Data.request(Bob)
Data.request(!)
Data.ind(!)
Data.ind(Bob)
Data.req(Nice to meet you)
Data.ind(Nice to meet you)
Data.ind(Bob)

## Slide 48: Exchanging datagrams
What type of data can be exchanged ?
  A datagram is sequence of bytes
How to exchange structured information ?
  Integers
  Floating point numbers
  structures

## Slide 49: Little and big endian
How are integers stored in memory ?
For Internet protocols, integers are big-endian
  Use htonl, ntohl and related functions
Source : https://en.wikipedia.org/wiki/Endianness

## Slide 50: Representing datagrams containing binary data
Short integer
Flags
32 bits
IPv4 address
IPv6 Address
Long integer
Char
Type
Length
Padding
Variable length field
16 bits
8 bits
8 bits
32 bits
32 bits
128 bits
8 bits
8 bits
8 bits
length bytes

## Slide 51: Reliable Bytestream
Three phases
  Connection establishment
    Communicating hosts agree to create two bytestreams, one per direction
  Data transfer
  Connection release

## Slide 52: Connection establishment
Source
Network provider
Destination
CONNECT.request
CONNECT.indication
CONNECT.confirm
Source considers
connection open
CONNECT.response
Destination considers connection open

## Slide 53: Connection refused
Source
Network provider
Destination
CONNECT.request
CONNECT.indication
DISCONNECT.indication
DISCONNECT.request

## Slide 54: Connection impossible
Source
Network provider
Destination
CONNECT.request
DISCONNECT.indication

## Slide 55: Data transfer Message mode
Source
Provider
Destination
CONNECT.request
CONNECT.indication
CONNECT.confirm
CONNECT.response
DATA.request("A")
DATA.ind("A")
DATA.request("BCD")
DATA.ind("BCD")
DATA.request("EF")
DATA.ind("EF")

## Slide 56: Data transfer Stream mode
Source
Provider
Destination
CONNECT.request
CONNECT.indication
CONNECT.confirm
CONNECT.response
DATA.ind("B")
DATA.ind("A")
DATA.request("AB")
DATA.request("CD")
DATA.ind("C")
DATA.request("EF")
DATA.ind("DEF")

## Slide 57: Abrupt release
Source
Provider
Destination
DISCONNECT.req(abrupt)
DISCONNECT.indication
DATA.request("A")
DATA.request("B")
DATA.indication("A")
DATA.request("C")
Connection opened
Connection opened
Can also be caused by the network
(e.g. network cannot anymore receive
packets from peer)

## Slide 58: Abrupt release triggered by the network
Source
Provider
Destination
DISCONNECT.indication
DISCONNECT.indication
DATA.request("A")
DATA.request("B")
DATA.indication("A")
DATA.request("C")
Connection opened
Connection opened

## Slide 59: Graceful release
Source
Provider
Destination
DISCONNECT.req(graceful)
DISCONNECT.ind(graceful)
Connection opened
Connection opened
DATA.request("A")
DATA.request("B")
DATA.indication("A")
DATA.indication("B")
DATA.request("C")
DATA.indication("C")
Source->Destination connection closed
DATA.request("D")
DATA.indication("D")
DISCONNECT.req(graceful)
Connection closed
DISCONNECT.ind(graceful)
Connection closed

## Slide 60: Internet Transport services
Service provided by UDP
  Connectionless, unreliable
Service provided by TCP
  Connection-oriented
  reliable bytestream

## Slide 61: Multiplexing
How to multiplex data coming from multiple applications on a single host having a single IP address ?

## Slide 62: Multiplexing
Server
Client
Source port : 1234
Destination port: 5678
Request
Response
Source port : 5678
Destination port: 1234
Source Addr: Client
Dest. Addr: Server
Source Addr: Server
Dest. Addr: Client

## Slide 63: UDP protocol
Source Port
Destination port
UDP length
UDP Checksum
8 bytes
Payload
32 bits
Constraint
Each UDP segment must fit inside a single IP packet
Used to identify the application that will receive this segment on destination host
Checksum computed over the entire UDP segment and part of the IP header to detect transmission errors.
0 means that the sender did not compute a checksum.
Used to identify the application that sent this segment on sending host
IP Packet
Notes: The computation of the UDP checksum is defined in :
R. Braden, D. Borman, C. Partridge, Computing the Internet Checksum, RFC1071, Septembre 1988

## Slide 64: UDP ports
Server
Client
Source port : 1234
Destination port: 5678
Request
Response
Source port : 5678
Destination port: 1234

## Slide 65: UDP Applications
Among these applications, which typically use UDP ?
  Voice over IP
  ssh
  web
  Microsoft Teams
  Netflix

## Slide 66: Usage of UDP
Request-response applications
  DNS, RPC, NFS, ..
Applications with short delay
  Games
Multimedia transfer
  Voice over IP
  Video over IP

## Slide 67: Multiplexing
Server
Client
Source port : 1234
Destination port: 5678
Request
Response
Source port : 5678
Destination port: 1234

## Slide 68: Connection table
A server interacts with many different clients and maintains a connection table
  This table contains one entry per active connection with its state
  Each connection is identified by 4 infos
    Client address and port
    Server address and port

## Slide 69: Datagram - UDP
UDP service
Applic. 2
Applic. 1
Identification
IP address : 2001:4860:a005::68
Protocol : UDP
Port : 53
Identification:
IP address : 2001:6a8:3080:2:217:f2ff:fed6:65c0
Protocol : UDP
Port : 1234
Identification of an application
  IP address + port number
Notes: UDP is defined in
J. Postel, User Datagram Protocol. RFC768, August 1980
It will be described in more details later

## Slide 70: Bytestream - TCP
  Identification of an application
    IP address + TCP + port number
TCP service
Applic. 2
Applic. 1
Identification
IP address: 2001:6a8:3080:1::3
Protocol : TCP
Port : 80
Identification:
IP address : 2a02:2788:2c4:16f:226:bbff:fe09:266e
Protocol : TCP
Port : 9876
Notes: TCP is defined in
J. Postel, Transmission Control Protocol, RFC793, September 1981
It will be described in more details later

## Slide 71: Agenda
Internet applications
  DNS
  Email
  Web

## Slide 72: Naming and addressing
address
  A (usually) fixed-length bit string that uniquely identifies a device (or an interface) in a network
name
  A human understandable name that identifies a device in a network

## Slide 73: Names and addresses
Different types of relations between names and addresses
  One-to-one
    A unique name corresponds to each unique address
  One-to-many
    A name corresponds to several addresses
  Many-to-one
    Several names correspond to the same address

## Slide 74: Names
How can we assign unique and non-ambiguous names to devices ?

## Slide 75: The tree of names
At each level, a secretariat verifies that domain names are unique
  A bit more than 1200 TLDs

## Slide 76: Domain names
Each domain name is a series of strings separated by dots
First version of DNS. Modern DNS supports unicode

## Slide 77: Mapping names to addresses
How to map names to addresses ?
First approach
  Distribute a file containing the mapping to all hosts
https://en.wikipedia.org/wiki/Hosts_%28file%29
See /etc/hosts on Unix

## Slide 78: The Domain Name System A distributed database
Each domain is managed by a name server which can:
  map a local name to an address
  return the name of a name server that is responsible for a domain

## Slide 79: How to query a name server ?
Which service would you use to query a name server ?
  Reliable connection oriented (TCP)
  Unreliable connectionless (UDP)

## Slide 80: DNS Resource Records
A
  IPv4 address
AAAA
  IPv6 address
NS
  Name server
Other specific records : CNAME, MX, TXT, ...
Each RR is structured as
Type
  Length
Value
TTL
Notes: The RR MX were proposed in
C. Partridge. Mail routing and the domain system. Request for Comments 974, Internet Engineering Task Force, January 1986.
A complete list of DNS RR may be found at
http://www.its.uq.edu.au/tn-0011

## Slide 81: The root DNS servers
Thirteen servers that know the name servers that are responsible for the Top-Level-Domain names

## Slide 82: The Root Servers

## Slide 83: Example
Resolve www.google.com
Try to resolve www.computer-networking.info starting from the root from home

## Slide 84: DNS resolution (1)
NS ? com
Root
2001:dc3::35
NS -> m.gtld-servers.net. Additional m.gtld-servers.net = 2001:501:b1f9::30
NS ? Google.com
Com NS
2001:501:b1f9::30
NS -> ns1.google.com.
Additional: ns1.google.com = 2001:4860:4802:32::a
AAAA ? www.google.com
AAAA -> 2a00:1450:4009:80a::2004
Google.com NS
2001:4860:4802:32::a
www.google.com

## Slide 85: DNS resolution (1)
NS ? info
Root
2001:dc3::35
NS -> a0.info.afilias-nst.info. Additional a0..info = 2001:500:19::1
NS ? Computer-networking.info
Info NS
2001:500:19::1
NS -> ns20.ovh.net
NS ? net
NS -> m.gtld-servers.net. Additional m..net = 2001:501:b1f9::30
www.computer-networking.info

## Slide 86: DNS resolution (2)
NS ? ovh.net
NS ? Ns10.ovh.net. Additional ns10.ovh.net = 2001:41d0:1:1981::1
AAAA ? Ns20.ovh.net
Net NS
2001:501:b1f9::30
AAAA -> 2001:41d0:1:198f::1
AAAA ? www.computer-networking.info
CNAME cnp3book.info.ucl.ac.be
Ns20.ovh.net
2001:41d0:1:198f::1
OVH NS
2001:41d0:1:1981::1
www.computer-networking.info

## Slide 87: DNS resolution (3)
NS ? be
Root
2001:dc3::35
NS -> d.nsset.be.
Additional d.nsset.be = 2001:678:6c::1
NS ? Ac.be
Be NS
2001:678:6c::1
NS -> ns1.belnet.be.
Additional : 2001:6a8:3c80::14
NS ? Ucl.ac.be
NS -> ns1.belnet.be
NS -> ns1.sri.ucl.ac.be
Ac.Be NS
2001:6a8:3c80::14
www.computer-networking.info

## Slide 88: DNS resolution (4)
NS ? Info.ucl.ac.be
NS -> dnssrv.info.ucl.ac.be.
Additional dnss..be = 2001:6a8:308f:1::d
AAAA ? Cnp3book.info.ucl.ac.be
cnp3book.info.ucl.ac.be. CNAME mptcp.info.ucl.ac.be.
mptcp.info.ucl.ac.be. AAAA 2001:6a8:308f:8:0:82ff:fe68:e48c
Ucl.ac.Be NS
2001:6a8:3c80::14
Info.ucl.ac.Be NS
2001:6a8:308f:1::d
www.computer-networking.info

## Slide 89: Root servers
Which questions are valid for root servers ?
dig -t NS net @2001:dc3::35
dig -t AAAA www.uclouvain.be @2001:dc3::35
dig -t NS be @2001:dc3::35 dig -t A dns.be @2001:dc3::35
;; QUESTION SECTION:
;be. IN NS
;; AUTHORITY SECTION:
be. 172800 IN NS c.nsset.be.
be. 172800 IN NS d.nsset.be.
;; ADDITIONAL SECTION:
d.nsset.be. 172800 IN A 194.0.44.1
c.nsset.be. 172800 IN A 194.0.43.1
d.nsset.be. 172800 IN AAAA 2001:678:6c::1
c.nsset.be. 172800 IN AAAA 2001:678:68::1

## Slide 90: DNS messages
Identification
Flags
32 bits
Number of additional
Number of authority
Number of answers
12 bytes
Questions
(variable number of resource records)
Number of questions
Answers
(variable number of resource records)
Authority
(variable number of resource records)
Additional information
(variable number of resource records)
Question/Response
Recursive question or not
Authoritative answer or not
Possible error
What is the role of the identification field ?

## Slide 91: DNS messages
Identification
Flags
32 bits
Number of additional
Number of authority
Number of answers
12 bytes
Questions
(variable number of resource records)
Number of questions
Answers
(variable number of resource records)
Authority
(variable number of resource records)
Additional information
(variable number of resource records)
Each DNS request contains a number that will be returned in the
response by the server to allow the client to match the request.
Question/Response
Recursive question or not
Authoritative answer or not
Possible error

## Slide 92: DNS Resource Records
Each DNS messages is composed of resource records (RR) encoded as TLV
  < Name, Value, Type, TTL>
  Types of RR
    A (Address)
      Name is a hostname and Value an IPv4 address
    AAAA (Address)
      Name is a hostname and Value an IPv6 address
    NS (NameServer)
      Name is a domain name and Value is the hostname of the DNS server responsible for this domain
    MX (Mail Exchange)
      Name is a domain name and Value is the name of the SMTP server that must be contacted to send emails to this domain
    Type CNAME
      Alias

## Slide 93: Using wireshark with DNS

## Slide 94: Example
dig -t AAAA www.ietf.org @2001:6a8:3081:1::53
; <<>> DiG 9.10.2-P1 <<>> -t AAAA www.ietf.org @2001:6a8:3081:1::53
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 33225
;; flags: qr rd ra ad; QUERY: 1, ANSWER: 3, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 4096
;; QUESTION SECTION:
;www.ietf.org. IN AAAA
;; ANSWER SECTION:
www.ietf.org. 1215 IN CNAME www.ietf.org.cdn.cloudflare-dnssec.net.
www.ietf.org.cdn.cloudflare-dnssec.net. 71 IN AAAA 2400:cb00:2048:1::6814:55
www.ietf.org.cdn.cloudflare-dnssec.net. 71 IN AAAA 2400:cb00:2048:1::6814:155
;; Query time: 1 msec
;; SERVER: 2001:6a8:3081:1::53#53(2001:6a8:3081:1::53)
;; WHEN: Thu Oct 15 12:05:47 CEST 2015
;; MSG SIZE rcvd: 149

## Slide 95: Packets exchanged
sudo tcpdump -n -i en4 -vv udp port 53
tcpdump: listening on en4, link-type EN10MB (Ethernet), capture size 262144 bytes
09:16:50.749400 IP6 (flowlabel 0x8ea5d, hlim 64, next-header UDP (17)
payload length: 38)
2001:6a8:3080:2:2908:3cb4:bbb4:ae0e.56551 > 2001:4860:4860::8888.53:
36945+ A? www.ietf.org. (30)
09:16:50.769351 IP6 (hlim 55, next-header UDP (17) payload length: 115)
2001:4860:4860::8888.53 >
2001:6a8:3080:2:2908:3cb4:bbb4:ae0e.56551:
36945 q: A? www.ietf.org. 3/0/0 www.ietf.org. CNAME www.ietf.org.cdn.cloudflare.net., www.ietf.org.cdn.cloudflare.net. A
104.20.1.85, www.ietf.org.cdn.cloudflare.net. A 104.20.0.85 (107)

## Slide 96: DNS in practice
Most users do not interact directly with root DNS resolvers
Enterprise, ISPs deploy DNS resolvers
  Servers that perform recursive DNS queries
dig -t A www.google.com +short @@ns1.sri.ucl.ac.be
142.250.184.228

## Slide 97: DNS Resolvers
Local resolvers inside UCLouvain
  130.104.230.68
  130.104.1.1
  130.104.1.2
  2001:6a8:3081:1::53
Open DNS resolvers
  8.8.8.8, 1.1.1.1, 9.9.9.9
  2001:4860:4860::8888, ...

## Slide 98: Example
dig www.ietf.org @2001:4860:4860::8888
; <<>> DiG 9.8.3-P1 <<>> www.ietf.org @2001:4860:4860::8888
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 36945
;; flags: qr rd ra; QUERY: 1, ANSWER: 3, AUTHORITY: 0, ADDITIONAL: 0
;; QUESTION SECTION:
;www.ietf.org. IN A
;; ANSWER SECTION:
www.ietf.org. 1441 IN CNAME www.ietf.org.cdn.cloudflare.net.
www.ietf.org.cdn.cloudflare.net. 43 IN A 104.20.1.85
www.ietf.org.cdn.cloudflare.net. 43 IN A 104.20.0.85
;; Query time: 39 msec
;; SERVER: 2001:4860:4860::8888#53(2001:4860:4860::8888)
;; WHEN: Tue Oct 21 09:16:50 2014
;; MSG SIZE rcvd: 107
What is a CNAME record ?

## Slide 99: DNS spoofing attack
What is this attack ?
How to counter it ?
dig porttest.dns-oarc.net TXT @2001:6a8:3081:1::53 +short
porttest.y.x.w.v.u.t.s.r.q.p.o.n.m.l.k.j.i.h.g.f.e.d.c.b.a.pt.dns-oarc.net.
"130.104.1.1 is GREAT: 26 queries in 3.8 seconds from 26 ports with std dev 15934"

## Slide 100: Agenda
Protocol stack
Internet applications
  DNS
  Email
  Web

## Slide 101: Simplified architecture
Bob@b.net
Alice@a.net
Alice’s email server
b.net ‘s email server
Alice sends her email to local mail forwarder
Alice’s server sends email to b.net’s MX
Bob retrieves message from his server

## Slide 102: Message format
Exp: ABC S.A.
Rue de Fer 10
5000 Namur
DEF Corp.
Steel street 9
WA78 AX London
Grande Bretagne
From: president@abc.be
To: ceo@def.com
Subject: Hello
Date : 27 Sept. 1999 0901
Dear Sir,
Bla Bla Bla...
Header
Message body

## Slide 103: Email message format
An email message is a series of ASCII lines
The first lines are the header lines that indicate control information

## Slide 104: Header format
At least three lines that end with <CRLF>
  From: sender@domain
  To:recipient@domain
  Date: <creation date of message>
Optional fields
  Subject: , cc: ,Message-ID:, Received: In-Reply-To: , ...
Header ends with empty line (<CRLF>)

## Slide 105: Sample messages

## Slide 106: MIME
Multipurpose Internet Mail Extensions
  Constraints
    must remain compatible with old email servers
      short US-ASCII Lines
    must support non-English text
    must support various formats
    must allow to transmit audio, video, ..
Notes: MIME was defined in
N. Freed and N. Borenstein. Multipurpose internet mail extensions (MIME) part one: Format of internet message bodies. Request for Comments 2045, Internet Engineering Task Force, November 1996.
N. Freed and N. Borenstein. Multipurpose internet mail extensions (MIME) part two: Media types. Request for Comments 2046, Internet Engineering Task Force, November 1996.

## Slide 107: MIME (2)
New header fields
  MIME-Version:
    version of MIME used to encode message
  Content-Description:
    comment describing the content of the message
  Content-Type:
    type of information inside message
  Content-Transfer-Encoding:
    how the message has been encoded
  Content-Id:
    unique identifier for the content

## Slide 108: MIME: Content-Type
Content-Type : type/encoding
  type of content
    text, image, video, application
    multipart
  encoding of content
    text/plain , text/html, image/gif, image/jpeg , audio/basic, video/mpeg, video/quicktime, application/octet-stream, application/postscript
    multipart/alternative, multipart/mixed
      attachment

## Slide 109: Character sets
How to support rich character sets ?
  Content-Type: text/plain; charset=us-ascii
  Content-Type: text/plain; charset=iso-8859-1
    Character set suitable for Western European languages, defined by ISO, 8 bits per character
    Content-Type: text/plain; charset=unicode
    Universal character set

## Slide 110: Content encoding
  How to encode non-text data ?
    Base64
  Base64
  uses ASCII characters A...Z,a...z,0...9, "+" et "/"
    A=0, B=1, C=2, ... +=62 et /=63
  Each character is used to encode 6 bits
    24 bits from initial message -> 4 ASCII characters
  Special character “=” used for padding

## Slide 111: Multipart/mixed
Date: Mon, 20 Sep 1999 16:33:16 +0200
From: Nathaniel Borenstein <nsb@bellcore.com>
To: Ned Freed <ned@innosoft.com>
Subject: Test
MIME-Version: 1.0
Content-Type: multipart/mixed; boundary="simple boundary"
preamble, to be ignored
--simple boundary
Content-Type: text/plain; charset=us-ascii
partie 1
--simple boundary
Content-Type: text/plain; charset=us-ascii
partie 2
--simple boundary
Notes: Exemple de message MIME
Received: from loriot.info.fundp.ac.be (loriot.info.fundp.ac.be [138.48.32.96])
by leibniz.info.fundp.ac.be (8.9.1/8.9.1) with SMTP id QAA19679;
Mon, 20 Sep 1999 16:37:25 +0200 (MET DST)
Message-Id: <3.0.5.32.19990920163316.00866340@info.fundp.ac.be>
Date: Mon, 20 Sep 1999 16:33:16 +0200
To: pers-aca, pers-sci
From: Gysele HENRARD <ghe@info.fundp.ac.be>
Subject: listes
Mime-Version: 1.0
Content-Type: multipart/mixed;
boundary="=====================_937830796==_"
--=====================_937830796==_
Content-Type: text/plain; charset="iso-8859-1"
Content-Transfer-Encoding: quoted-printable
Bonjour,
Voici des listes de 1M-1L, 2M-2L et ERASMUS mises =E0 jour ce lundi 20
septembre.
Gyselle
--=====================_937830796==_
Content-Type: application/octet-stream; name="1M_99_00.xls";
x-mac-type="584C5334"; x-mac-creator="5843454C"
...

## Slide 112: Email protocols
Bob@b.net
Alice@a.net
a.net’s SMTP server
b.net’s SMTP server
SMTP
Email retrieval
SMTP
Email retrieval:
POP
IMAP
Web interface
File access (/var/mail on Unix)

## Slide 113: SMTP : sending email
S: 220 smtp.example.com ESMTP Postfix
C: HELO relay.example.org
S: 250 Hello relay.example.org, I am glad to meet you
C: MAIL FROM:<bob@example.org>
S: 250 Ok
C: RCPT TO:<alice@example.com>
S: 250 Ok
C: RCPT TO:<theboss@example.com>
S: 250 Ok
C: DATA
S: 354 End data with <CR><LF>.<CR><LF>
C: From: "Bob Example" <bob@example.org>
C: To: "Alice Example" <alice@example.com>
C: Cc: theboss@example.com
C: Date: Tue, 15 Jan 2008 16:02:43 -0500
C: Subject: Test message C: C: Hello Alice.
C: This is a test message with 5 header fields and 4 lines in the message body.
C: Your friend,
C: Bob
C: .
S: 250 Ok: queued as 12345
C: QUIT
S: 221 Bye
Client opens TCP connection with server port 25

## Slide 114: POP : retrieving email
S: +OK POP3 server ready <1896.697170952@dbc.mtview.ca.us>
C: APOP mrose c4c9334bac560ecc979e58001b3e22fb
S: +OK mrose's maildrop has 2 messages (320 octets)
C: STAT
S: +OK 2 320
C: LIST
S: +OK 2 messages (320 octets)
S: 1 120
S: 2 200
S: .
C: RETR 1
S: +OK 120 octets
S: <the POP3 server sends message 1>
S: .
C: DELE 1
S: +OK message 1 deleted
C: DELE 2
S: +OK message 2 deleted
C: QUIT
S: +OK dewey POP3 server signing off (maildrop empty)
Client opens TCP connection with server port 110

## Slide 115: Agenda
Protocol stack
Internet applications
  DNS
  Email
  Web

## Slide 116: Question
When (year) were the first public web servers launched ?

## Slide 117
https://home.cern/science/computing/birth-web/short-history-web

## Slide 118: Internet versus web
https://www.reddit.com/r/pcmasterrace/comments/b086lz/tim_bernerslee_and_vint_cerf_wearing_funny_shirts/

## Slide 119: Simplified architecture
Client
(browser)
Server www.machin.be
Server www.truc.fr
Query
Information

## Slide 120: Key elements of the web
URL : An addressing scheme that allows to identify any document stored on a server
HTML : hypertext language to easily write documents with hypertext links
HTTP : An efficient and lightweight protocol to exchange documents
Servers
Clients (browsers)

## Slide 121: URL
syntax : <protocol>://<document>
  http is the most common
  https implies added security (see later)
  document indicates the server and the location of the document
  <user>:<password>@<server>:<port>/<path>

## Slide 122: HTML
<HTML>
<HEAD>
<TITLE>HTML test page</TITLE>
</HEAD>
<BODY>
<IMG SRC="http://www.images.be/logo.gif">
<H1>Web servers from UCL UCL<P></H1>
<HR>
<UL>
<LI><A HREF="http://www.uclouvain.be">UCL</A>
<LI><A HREF="http://www.info.ucl.ac.be">CSE Dept.</A>
<LI><A HREF="http://www.math.ucl.ac.be">Math</A>
</UL>
</BODY>
</HTML>
Header
Body
Image on remote server
First level title
External hypertext link

## Slide 124: HTTP
Client
Server
Method
Header
CRLF
MIME Document
Request
Method
GET
POST
...
Header contains additional information about request sent by client
Status line
Header
CRLF
MIME Document
Response
Header contains information about server
and optional parameters specific to response
Success or failure
HTTP is a stateless protocol, server does not maintain any state from one request to another

## Slide 125: HTTP
Which transport service would you select to support HTTP ?
  Unreliable connectionless service (UDP)
  Reliable bytestream connection-oriented (TCP)

## Slide 126: HTTP/1.0
HTTP 1.0 - non-persistent connection
Client
Server
CONNECT.request
CONNECT.indication
CONNECT.confirm
CONNECT.response
DATA.request(Request)
DATA.req(Response)
DATA.ind(Request)
DATA.ind(Response)
DISCONNECT.ind
DISCONNECT.req
DISCONNECT.req
DISCONNECT.ind
Notes: HTTP 1.0 is defined in :
T. Berners-Lee, R. Fielding, and H. Frystyk. Hypertext transfer protocol -- HTTP/1.0. Request for Comments 1945, Internet Engineering Task Force, May 1996.

## Slide 127: HTTP : Methods
Methods
  GET
    method used to request a "document" stored on server
      GET <document> HTTP/1.0
  POST
    method used to send a "document" to a server
      document is part of the request and encoded as a MIME document

## Slide 128: Request headers
  Host: <name>
    Name of the server where the document is stored
  Authorization
    allows to perform access control
  If-Modified-Since: <date>
    server will only send if more recent than date
  Referer: <url>
    URL visited by the client before this request
  User-Agent: <agent>
    client’s browser

## Slide 129: HTTP : Status line
Format : Version_HTTP Code Comment
  Success/Failure
    2xx : Success
      Example : HTTP/1.0 200 OK
    3xx : Redirection
    4xx : Client-side error
    5xx : Server-side error

## Slide 130: HTTP Response
Date
  date of the document attached to response
Server
  Name and version of http server used
Content-*
  MIME header of the attached document

## Slide 131: HTTP : Example
Client
Server
www.example.org
  GET / HTTP/1.1
  Host: www.example.org
  User-Agent: curl/7.64.1
  Accept: */*
  CRLF
Request
Response
HTTP/1.1 200 OK
Cache-Control: max-age=604800
Content-Type: text/html; charset=UTF-8
Date: Wed, 08 Feb 2023 19:08:16 GMT
Expires: Wed, 15 Feb 2023 19:08:16 GMT
Last-Modified: Thu, 17 Oct 2019 07:18:26 GMT
Server: ECS (nyb/1D2B)
Content-Length: 1256
CRLF
<HTML>
. . .
</HTML>
curl -v http://www.example.org

## Slide 132: HTTP 1.1
HTTP 1.0
  a single TCP connection is used to transmit a single document (html file, image,...)
HTTP 1.1
  uses a single persistent TCP connection
    This TCP connection can be used for several requests and the corresponding responses
    the cost of establishing and releasing the TCP connection is amortised over multiple requests
    Although HTTP 1.1 uses a single TCP connection for multiple requests, HTTP 1.1 remains stateless
Notes: HTTP 1.1 is defined in :
R. Fielding, J. Gettys, J. Mogul, H. Frystyk, L. Masinter, P. Leach, and T. Berners-Lee. Hypertext transfer protocol -- HTTP/1.1. Request for Comments 2616, Internet Engineering Task Force, June 1999.

## Slide 133: HTTP 1.1
Client
Server
CONNECT.request
CONNECT.indication
CONNECT.confirm
CONNECT.response
DISCONNECT.ind
DISCONNECT.req
DISCONNECT.req
DISCONNECT.ind
HTTP/1.1 200 OK
Keep-Alive: timeout=15, max=99
Connection: Keep-Alive
...
GET / HTTP1.1
Connection: Keep-Alive
...
HTTP/1.1 200 OK
Keep-Alive: timeout=15, max=100
Connection: Keep-Alive
...
GET /images/logo.gif HTTP1.1
Connection: Keep-Alive
...

## Slide 134: HTTP Authentication
Client
Server
HTTP/1.0 401 Authorization req
WWW authenticate: machin
...
GET / HTTP1.1
...
Browser asks user/password to user
HTTP/1.1 200 OK
...
GET / HTTP1.1
Authorization: User-password
...
GET /images/t.gif HTTP1.1
Authorization: User-password
...
Browser sends user/password in each request

## Slide 135: HTTP Cookies
Client
Server
HTTP/1.0 200 OK
Set-Cookie: machin
...
GET / HTTP1.1
...
Browser saves cookie
HTTP/1.1 200 OK
...
GET /doc HTTP1.1
Cookie: machin
...
GET /images/t.gif HTTP1.1
Cookie: machin
...
Browser sends cookie in all requests sent to server
Response is function of URL and cookie
Normal response

## Slide 136: The Host header One server many sites
Server:
www.gembloux.be
www.olln.be
$dig +short www.olln.be
site-ottignieslouvainlaneuve.imio.be.
lb.imio.be.
188.165.186.183, 188.165.186.179
$ dig +short www.gembloux.be
site-gembloux.imio.be.
lb.imio.be.
188.165.186.179, 188.165.186.183

## Slide 137: A single physical server for many TLS services
Server Name Indication
Alice
Bob
ClientHello (SNI=bob.be Ciphers, RandomAlice)‏
ServerHello(Ciphers,RandomBob )‏
Certificate(PubBob , PrivC )‏
PubC, ,PubBob,,PrivBob
S(PubBob , PrivC )‏
PubC,
E( PreMasterSecret , PubBob)‏
Alice chooses PreMaster Secret
Finished( H(handshake msgs,Key)‏
Finished( H(handshake msgs,Key))‏
Tom
PubC, ,PubTom,,PrivTom
S(PubTom , PrivC )‏

## Slide 138: HTTPS versus HTTP

## Slide 139: Question
What is the average size of a web page (in bytes) ?

## Slide 140
https://httparchive.org/reports/state-of-the-web#bytesTotal

## Slide 141: How many HTTP requests per page ?
Source: httparchive.org

## Slide 142: Today's web pages
Source: https://httparchive.org/reports/page-weight.org
Can you order the different elements of web pages in terms of importance ( smallest average volume first) ?
  CSS
  Font
  HTML
  Images
  Javascript
  Video
  HTML
  CSS
  Font
  Javascript
  Images
  Video

## Slide 143
https://amelie.info.ucl.ac.be

## Slide 144: Practical session sockets programming

## Slide 145: For next week
Read the sections covered today
  Applications, Transport Service
  Application Layer
    DNS, Email, HTTP
Prepare next week’s topic
  Making HTTP faster
  Security