## Slide 1: Part 10 Congestion control
O. Bonaventure, 2016-2022

## Slide 2: Agenda
Congestion Control
  Principles
  Additive Increase/Multiplicative Decrease
    Explicit Congestion Notification
    Modern TCP Congestion control
    Router behavior

## Slide 3: Adapting to different bandwidth
What is the round-trip-time in milliseconds in this network if A sends 10,000 bits segments, all links are 1 m long and B returns 100 bits acks ?
If A sends four 10,000 bits segments in a row, after how many msec will it receive the last ack ?

## Slide 4: Self-clocking

## Slide 5: The congestion problem
If R1 has a buffer of five 10,000 bits long packets, how many packets will be dropped if A and B send a burst of ten packets at line rate ?

## Slide 6: Fairness
How should bandwidth be distributed among different flows ?
  On a single link
    Fair share
  In a large network
    Max-min fairness

## Slide 7: Max-min fairness
a max-min allocation of bandwidth is an allocation of bandwidth which maximises the allocation of bandwidth to the sources receiving the smallest allocation
  a max-min fair allocation is such that in order to increase the bandwidth allocated to one source, it is necessary to decrease the bandwidth allocated to another source which already receives a lower allocation

## Slide 8: Max-min fairness
a max-min allocation maximises the allocation of bandwidth to the sources receiving the smallest allocation
Property
  to increase the bandwidth allocated to one source, it is necessary to decrease the bandwidth allocated to another source which already receives a lower allocation

## Slide 9: Example
    Max-min fair bandwidth allocation
R
R
R
R
R
1000 Mbps
100 Mbps
S1
S2
S3
S4
S5 S6 S7 S8
D1 D3 D4
D2
D5
D6
D7
D8
Link1
Link2
Link3
Link4
S3-D3 ?
S2-D2 ?
S1-D1 ?
Notes: How to determine a max-min fair bandwidth allocation for a given network ?
Algorithm [Bertsekas & Gallager, Data Networks, 2nd edition, Prentice Hall 1992]
First start with an allocation of 0 Mbps for each source
Then equally increment the allocation to each source until one link becomes saturated. At this point, each source which uses the saturated link receives an allocation equal to the bandwidth of this saturated link divided by the number of sources using this bottleneck link.
Next, the allocation of all the sources which do not use a saturated link is equally incremented until another link becomes saturated.
The algorithm continues from step to step, always incrementing the allocation of the sources which do not use a saturated link, until all sources use at least one of the saturated links.

## Slide 10: How to achieve max-min fairness ?
Two possible approaches
  Modify the routers to reach max-min fairness
  Modify the endhosts to reach max-min fairness

## Slide 11: How to detect congestion ?
Packet losses
Increased delay
Routers add information to packets
  Forward binary feedback
  Backward binary feedback
  Rate feedback

## Slide 12: Agenda
Congestion Control
  Principles
  Additive Increase/Multiplicative Decrease
  Explicit Congestion Notification
  Modern TCP Congestion control
  Router behavior

## Slide 13: The congestion problem
Bottleneck link
N Mbps
How to efficiently share the bandwidth ?

## Slide 14: Delay versus bandwidth
Bwi
observed
rtt
min rtt
buffer almost overloaded
huge packet losses

## Slide 15: Router buffers
Rule of thumb
  Routers should have RTT * C of buffers
      RTT is average rtt for flows
      C is bandwidth of output link
Backbone routers
N. McKeown, G. Appenzeller, I. Keslassy, Sizing Router Buffers (Redux), SIGCOMM CCR October 2019

## Slide 16: Congestion signals
Main types of congestion signals
  Packet loss
    most popular signal
  Explicit Congestion Notification
    requires router cooperation
  Increase in measured round-trip-time
    can be fragile

## Slide 17: Congestion control

## Slide 18: Congestion control
Additive Increase / Multiplicative Decrease
# Additive Increase Multiplicative Decrease
if congestion :
rate=rate*betaC # MD, betaC<1
else
rate=rate+alphaN # AI

## Slide 19: Additive Increase
No congestion ?
  All acks move window
Additive increase
  Increment cwnd by one MSS every rtt
Cwnd
Time

## Slide 20: Faster increase
How to speed up the growth of the congestion window at connection startup ?
Slow-start
  Double cwnd every rtt
Cwnd
Slow-start
exponential increase of cwnd
Time
Max window

## Slide 21: Multiplicative decrease
How to detect congestion ?
  Three duplicate acks
    mild congestion for TCP
      cwnd/2 and restart additive increase
  Expiration of retransmission timer
    severe congestion
    Reset cwnd at 1 MSS
    Perform slow-start until half previous cwnd and then continue with congestion avoidance

## Slide 22: TCP with mild congestion
Cwnd
Fast retransmit
Threshold
Threshold
Slow-start
exponential increase of cwnd
Congestion avoidance
linear increase of cwnd
Fast retransmit
Mild congestion

## Slide 23: Severe congestion
Cwnd
Time
Timer expiration
Threshold
Timer expiration
Threshold
Slow-start
exponential increase of cwnd
Congestion avoidance
linear increase of cwnd

## Slide 24: TCP with mild congestion
Cwnd
Fast retransmit
Threshold
Threshold
Slow-start
exponential increase of cwnd
Congestion avoidance
linear increase of cwnd
Fast retransmit

## Slide 25: Severe congestion
Cwnd
Time
Timer expiration
Threshold
Timer expiration
Threshold
Slow-start
exponential increase of cwnd
Congestion avoidance
linear increase of cwnd

## Slide 26: How to implement AIMD ?
Initialisation :
cwnd = MSS;
ssthresh= swin;
Ack reception :
if (network not congested ) // no segment losses
{
if (cwnd < ssthresh)
{ // increase quickly cwnd
// double cwnd every rtt
cwnd = cwnd+ MSS;
}
else
{ // increase slowly cwnd
// increase cwnd by one mss every rtt
cwnd = cwnd+ mss*(mss/cwnd);
}
}
Congestion avoidance
Slowstart

## Slide 27: AIMD in TCP
# Initialisation
cwnd = MSS ssthresh= swin dupacks=0
# Ack arrival (assumes no delayed acks)
if tcp.ack > snd.una : # new ack, no congestion
if dupacks==0: # not currently recovering from loss
if cwnd < ssthresh :
# slow-start : increase quickly cwnd
# double cwnd every rtt
cwnd = cwnd + MSS
else:
# congestion avoidance : increase slowly cwnd
# increase cwnd by one mss every rtt
cwnd = cwnd+ mss*(mss/cwnd)
else: # recovering from loss
cwnd=ssthresh # deflate cwnd rfc5681
dupacks=0

## Slide 28: Slow-start
cwnd=1000
ssthresh=64000
0-999
ACK(1000)
1000-1999
2000-2999
ACK(2000)
ACK(3000)
cwnd=2000
ssthresh=64000
cwnd=3000
ssthresh=64000
cwnd=4000
ssthresh=64000
3000-3999
4000-4999
5000-5999
6000-6999
ACK(4000)
ACK(7000)
cwnd ?

## Slide 29: Congestion avoidance
cwnd=2000
ssthresh=4000
1000-1999
2000-2999
ACK(2000)
ACK(3000)
cwnd=3000
ssthresh=4000
cwnd=4000
ssthresh=4000
cwnd=4000+(1000*1000/4000)=4250
3000-3999
4000-4999
5000-5999
6000-6999
ACK(4000)
ACK(7000)
cwnd=4250+(1000*1000/4250)=4485
cwnd=4485+(1000*1000/4485)=4707
cwnd=4707+(1000*1000/4707)=4919
cwnd ?

## Slide 30: AIMD in TCP
else: # duplicate or old ack
if tcp.ack==snd.una: # duplicate acknowledgment
dupacks++
if dupacks==1 or dupacks==2:
send_next_unacked_segment # rfc3042
if dupacks==3:
retransmitsegment(snd.una)
ssthresh=max(cwnd/2,2*MSS)
cwnd=ssthresh
if dupacks>3: # rfc5681
cwnd=cwnd+MSS # inflate cwnd
else: # ack for old segment, ignored
Expiration of the retransmission timer:
send(snd.una) # retransmit first lost segment
sshtresh=max(cwnd/2,2*MSS)
cwnd=MSS

## Slide 31: Examples
Time to transmit 6 TCP segments without losses
Time to transmit 6 TCP segments if 3rd is lost
Time to transmit 10 TCP segments if 5th is lost

## Slide 32: TCP and losses
cwnd=1000
0-999
ACK(1000)
1000-1999
2000-2999
ACK(2000)
cwnd=2000
cwnd=3000
3000-3999
4000-4999
ACK(2000)
ACK(2000)
cwnd=3000
dupack=1
cwnd=3000
dupack=2
write(5000 bytes)

## Slide 33: TCP and losses
cwnd=3000
dupack=2
2000-2999
RTO expires
cwnd=1000
dupack=0
ssthresh=2000
ACK(5000)
cwnd=2000
dupack=0

## Slide 34: TCP and losses
cwnd=1000
ssthresh=64000
0-999
ACK(1000)
1000-1999
2000-2999
ACK(2000)
ACK(3000)
cwnd=2000
ssthresh=64000
cwnd=3000
ssthresh=64000
cwnd=4000
ssthresh=64000
3000-3999
4000-4999
5000-5999
6000-6999
write(10000 bytes)

## Slide 35: TCP and losses
cwnd=4000
3000-3999
cwnd=2000
dupack=0
ssthresh=2000
ACK(9000)
7000-7999
8000-8999
ACK(3000)
ACK(3000)
ACK(3000)
dupack=1
dupack=2
dupack=3
9000-9999
ACK(10000)

## Slide 36: Simplified model
  Assume all segment losses are periodic and that every 1/p segment is lost
Cwnd(segments)
W
W/2
0
0 W/2 W 3W/2 2W time(rtt)
Surface
It can be shown that the throughput of a TCP
connection can be approximated by :
Maximum throughput without losses
Throughput with losses/congestion
Notes: More detailed models can be found in the scientific literature :
M. Mathis,J. Semke, J. Mahdavi and T. Ott, The macroscopic behaviour of the TCP congestion avoidance algorithm, ACM Computer Communication Review, 1997

## Slide 37: Agenda
Congestion Control
  Principles
  Additive Increase/Multiplicative Decrease
  Explicit Congestion Notification
  Modern TCP Congestion control
  Router behavior

## Slide 38: Limitations of packet drops
Router drops packets when it is congested
  The packets that are dropped by the congested router have already consummed resources upstream
How can we control congestion without dropping packets to inform the senders of the current level of congestion ?

## Slide 39: Basic ECN
Issues
  What happens if the returning ECN-echo is lost ?
  How can we deploy ECN?
R1
R2
A
D
Congestion Notification
Mark the IP packet that caused congestion by setting one bit flag (CE: Congestion Experienced)
TCP source behaviour
Upon reception of a ECN-Echo=1 TCP ack,
behave as if the corresponding segment was lost (perform congestion avoidance).
TCP destination behaviour
Upon reception of a CE=1 IP packet indicate the congestion to the source by setting a special
flag (ECN-Echo) in the returning TCP ack

## Slide 40: Dealing with lost acks

## Slide 41: Deploying ECN
On endhosts
  Update the TCP stack to support ECN
    Negotiate ECN usage in SYN
    Encode ECN info in packets/segments
  For other transport protocols…

## Slide 42: Deploying ECN
On routers
  Routers need to distinguish between
    ECN-capable hosts that react to ECN
      If congestion, such packets are marked
    Other hosts that do not react to ECN
      If congestion, such packets are dropped

## Slide 43: ECN support on routers
Specialised buffer acceptance algorithms
R1
R2
A
D
In case of congestion
If ECT bit is set
Mark the IP packet that caused congestion by setting on bit flag (CE: Congestion Experienced)
If ECT bit is not set
Discard the IP packet that caused congestion
ECN-capable source
If destination is also ECN capable
Set ECT bit in all IP packets towards destination
Otherwise
Reset ECT bit

## Slide 44
http://www.ietf.org/proceedings/94/slides/slides-94-hopsrg-7.pdf

## Slide 45: Agenda
Congestion Control
  Principles
  Additive Increase/Multiplicative Decrease
  Explicit Congestion Notification
  Modern TCP Congestion control
  Router behavior

## Slide 46: Issues with AIMD
Performance on high bandwidth*delay links
  Each loss forces TCP in congestion avoidance and grows slowly
Bufferbloat
  TCP AIMD tries to saturate buffers until it causes congestion
  Inflates round-trip-times
Fairness
  TCP sources with a lower rtt are favored

## Slide 47: Tuning TCP @google
Objectives
  Minimize time to receive result from search engine
    HTTP GET fits a single segment
    HTTP Response in <16 KBytes

## Slide 48: Initial congestion window
What is the impact of initial congestion window and the slow-start on the time to receive an HTTP response ?

## Slide 49: Initial TCP congestion window today
Source: M. Bagnulo, tcpmp mailing list, Nov 16th, 2016

## Slide 50: TCP Congestion Controls
Supposed to be fair
  MSS size
  rtt
Many congestion control schemes
Source: B. Turkovic, F. Kuipers and S. Uhlig, Fifty Shades of Congestion Control: A Performance
and Interactions Evaluation, https://arxiv.org/pdf/1903.03852.pdf

## Slide 51: CUBIC
A modern congestion controller designed for high bandwidth*delay product links
  Default on Linux, Apple and Microsoft
Principles
  Use concave and convex profiles of cubic function to increase cwnd
  CUBIC behaves like AIMD with small rtt/bw
  CUBIC provides linear bandwidth sharing among flows with different rtt

## Slide 52: CUBIC
Congestion window increase during congestion avoidance
Source: B. Turkovic, F. Kuipers and S. Uhlig, Fifty Shades of Congestion Control: A Performance
and Interactions Evaluation, https://arxiv.org/pdf/1903.03852.pdf and RFC8312
cwnd=+ C
Packet loss:
max=
cwnd=
Parameters

## Slide 53: Bottleneck Bandwidth and Round-Trip-Time (BBR)
Recent congestion control scheme that aims at achieving high throughput and low delay
Operates in four phases
Startup (similar to slow-start until measured rate stops increase)
Drain (empty the queues, send at 0.75 rate)
  compute rttmin over last 10 seconds
Probe bandwidth every 8 rtt (send at 1.25 rate for one rtt and then at 0.75 rate)
Probe RTT (reduce rate for more precise rttmin)

## Slide 54: Reno, CUBIC, BBR
Cwnd
ssthresh
Slow-start
exponential increase of cwnd
Congestion avoidance
linear increase of cwnd

## Slide 55: Reno, CUBIC, BBR
Cwnd
Slow-start
exponential increase of cwnd
Congestion avoidance
ssthresh
W_max

## Slide 56: Reno, CUBIC, BBR
Cwnd
Startup
Congestion avoidance
Fast retransmit

## Slide 57: Delay-based techniques
TCP Vegas : intuition
  Expected rate =
  Estimate buffer size at bottleneck every rtt
    if => cwnd=cwnd-MSS //congestion
    if => cwnd=cwnd+MSS // increase

## Slide 58: CUBIC, Vegas and BBR
Source: B. Turkovic, F. Kuipers and S. Uhlig, Fifty Shades of Congestion Control: A Performance
and Interactions Evaluation, https://arxiv.org/pdf/1903.03852.pdf and RFC8312

## Slide 59: Two TCP connections
Source: B. Turkovic, et al., Fifty Shades of Congestion Control: A Performance
and Interactions Evaluation, https://arxiv.org/pdf/1903.03852.pdf

## Slide 60: Two TCP connections, different rtt
Source: B. Turkovic, et al., Fifty Shades of Congestion Control: A Performance
and Interactions Evaluation, https://arxiv.org/pdf/1903.03852.pdf

## Slide 61: Two different congestion controllers
Source: B. Turkovic, et al., Fifty Shades of Congestion Control: A Performance
and Interactions Evaluation, https://arxiv.org/pdf/1903.03852.pdf

## Slide 62: Agenda
Congestion Control
  Principles
  Additive Increase/Multiplicative Decrease
  Explicit Congestion Notification
  Modern TCP Congestion control
  Router behavior

## Slide 63: Traffic control techniques
What are the techniques that a single router can use to provide different types of services to different applications ?
  First step : identify the applications that need to obtain each service type
  Second step : allocate network ressources to the different applications

## Slide 64: Router output port
Output link
Input link 1
Input link N
Classifier
IP packets
IP packets
IP packets with internal ID

## Slide 65: How would you implement a classifier ?
Per source classification ?
  IP address, IP prefix, TCP/UDP ports ?
Per destination classification ?
  IP address, IP prefix, TCP/UDP ports ?
Per application classification ?

## Slide 66: Buffer Acceptance
How to decide which packets can be accepted inside the buffer ?
Buffer
Classification
Input links
Output link

## Slide 67: Buffer Acceptance
The two key questions for a buffer acceptance algorithm
  When should the BA algorithm decide to discard a packet ?
  Which packet should be discarded ?

## Slide 68: Buffer Acceptance Algorithms
Tail drop
  Arrival (Packet p) : if isFull(Buffer) then discard p; else AddTail(Buffer, p);
What are its advantages and drawbacks ?

## Slide 69: The traffic control building blockson router
Q[1]
Q[2]
Q[3]
Q[N]
Classification
Input links
Output link
Queuing strategy
Logical organisation of the
router's buffers
Scheduler
Chooses the packet to
be transmitted first on
the output link

## Slide 70: Priority scheduling
Flow 2, class B
Output buffer
Flow 1, class A
Flow 3, class B
Flow 4, class B
Flow N, class C
Class A
Class B
Class C
Packet transmission :
if (Queue(A) not empty)
serve Queue(A);
else
if (Queue(B) not empty)
serve Queue(B);
else
if (Queue(C) not empty)
serve Queue(C);
else ....

## Slide 71: Priority scheduling
With the priority scheduler, what is the ordering of the packets on the output link ?
A
D
B
E
F
C
High priority Queue
Medium Priority Queue
Low Priority Queue

## Slide 72: Round-Robin scheduling
Flow 2
Flow 1
Flow 3
Flow 4
Flow 5
Flow 1
Flow 2
Flow 3
Flow N
Scheduler :
F1
F2
F3
F4
FN

## Slide 73: Round robin
If the RR scheduler starts with queue1 and serves them in numerical order, what is the ordering of the packets on the output link ?
A
B
D
E
F
G
Queue 1
Queue 2
Queue 3

## Slide 74: Round-robin : example
F1
F2
F3
Flow2 (L=2)
Flow1(L=1)
Flow3 (L=1)
F1
F2
F3
Flow1 and Flow3 send packets of size 1
Flow 2 sends packets of size 2

## Slide 75: Example
F1
F2
F3
Flow2 (L=2)
Flow1(L=1)
Flow3 (L=1)
F1
F2
F3
Flow1 and Flow3 send packets of size 1
Flow 2 sends packets of size 2

## Slide 76: Round-Robin
Advantage
  Can provide fairness independently of the characteristics of the flows if flows use same packet size
Drawbacks
  Difficult to scale to a very large number of flows
  Unfair with different packet sizes

## Slide 77: Deficit Round-Robin
    associate counter d[i] to each queue
    increase d[i] by quantum every time queue[i] is visited
      if first_packet of queue[i] larger than d[i] { packet stays in queue[i]; }
else { packet is transmitted on output link; d[i]=d[i]- packet length; if queue[i] is empty { d[i]=0; } }
Flow 2
Flow 1
Flow 3
Flow 4
Flow 5
Flow 1
Flow 2
Flow 3
Flow N
Scheduler :
F1
F2
F3
F4
FN

## Slide 78: Deficit Round-Robin : example
F1
F2
F3
Flow2 (L=2)
Flow1(L=1)
Flow3 (L=1)
F1
F2
F3
Flow1 and Flow3 send packets of size 1
Flow 2 sends packets of size 2

## Slide 79: Deficit Round robin
If the DRR scheduler starts with queue1 and serves them in numerical order, what is the ordering of the packets on the output link ?
A
B
D
F
G
Queue 1
Queue 2
Queue 3

## Slide 80: Weighted Round-Robin
Flow 2
Flow 1
Flow 3
Flow 4
Flow 5
Flow 1
Flow 2
Flow 3
Flow 5
Scheduler :
F1
F2
F3
F4
F5
F1
F2
F1
F1
Fraction of the bandwidth for each flow ?

## Slide 81: Weighted Round-Robin
A : 25%
B : 50%
C : 25%
Line rate
Line rate
Variable
B's share
A's share

## Slide 82: Weighted Round Robin
A : 25%
B : 50%
C : 25%
Input Traffic pattern
  A : 20%, regular
  B: 60%
  C: 50%

## Slide 83: Weighted Round Robin
What is the impact of a burst of traffic ?
A : 75%
B : 24%
C : 1%
Input Traffic pattern
  A : 20%, regular
  B: 24%
  C: 100%