## Slide 1: Part 6 A QUIC introduction

## Slide 2: Projet - soumission
Première soumission
  Vendredi, cfr moodle. Nécessaire pour que l’on peut fixer les heures de presentation
  Soft deadline, vous pourrez amender votre presentation jusque la hard deadline
Hard deadline
  Jeudi 20 mars, 8h00
Présentation
  Vos slides (en pdf uniquement) seront sur les laptops des assistants pour minimizer le temps de changer de groupe

## Slide 3: Projet – grille d’évaluation de l’oral Volet forme (1/3)
Critère | Insuffisant | Suffisant | Bien | Très bien
Points clés | Le message ne passe pas du tout | Un point clé présenté, les autres restent flous | Deux points clés présentés | Tous les points importants sont clairs
Discours oral | Ne tient pas compte du public | Contact visuel continu | Présentation bien préparée et fluide | Captive son audience
Support visuel | Slides surcharges, vague, timing non respecté | Structure correcte de la presentation, slides appuient le discours | Slides pas trop chargés, figures utilisées intelligemment | Présentation agréable à suivre, grand soin apporté aux slides
Groupe | Pas de cohesion, une partie du groupe ne présente pas | Tous les étudiants parlent, mais certains répondent plus | Organisation du groupe pour répondre aux questions | Très bonne organisation du groupe, tous les étudiants maitrisent

## Slide 4: Projet – grille d’évaluation de l’oral Volet contenu (2/3)
Critère | Insuffisant | Suffisant | Bien | Très bien
DNS | Pas de réponse ou incorrect | Quelques éléments liés à la matière vue au cours | Réponse argumentée avec des paquets/analyse code source | Explication détaillée qui apporte un plus par rapport à ce qui a été vu au cours
UDP | idem | idem | idem | idem
TCP | idem | idem | idem | idem
IPv4/IPv6 | idem | idem | idem | idem
Sécurité/TLS | idem | idem | idem | idem
Extensions | idem | idem | idem | idem

## Slide 5: QUIC: a secure transport protocol
Initially proposed by Google to speedup HTTP
Main motivations
  Speedup HTTP
  Integrate security features
  Be easier to deploy by running above UDP
Standardized within IETF
https://www.ietf.org/proceedings/88/slides/slides-88-tsvarea-10.pdf
https://dl.acm.org/doi/pdf/10.1145/3098822.3098842

## Slide 6: QUIC A UDP-based multiplexed and secure transport
https://datatracker.ietf.org/doc/html/rfc9000

## Slide 7: QUIC deployment since March 2024
https://radar.cloudflare.com/adoption-and-usage?dateRange=52w

## Slide 8: Main characteristics of QUIC
Runs above UDP
  Allows QUIC to pass through middleboxes such as NAT that only understand TCP, UDP and ICMP
A single connection can efficiently carry multiple bytestreams
  Tuned to support HTTP/2 streams but much better than TCP
Same (or better) reliability and congestion control mechanisms as TCP
  Several improvements are possible thanks to QUIC’s design
Directly integrates all the security features of TLS
  QUIC provides better security than TLS above TCP
Connection migration
  On smartphones, a QUIC connection can migrate from cellular to Wi-Fi
QUIC can also be used to carry datagrams

## Slide 9: Protocol stack Physical layer
Unit of information : bit
Reliability
  transmission errors
  creation/suppression of bits
Physical
Physical
Physical
Types of physical layers
  Radio (Wi-Fi, cellular, Bluetooth,…)
  Optical fiber
  Cat5 cable
  Coaxial cable
  xDSL
  Modem

## Slide 10: Protocol stack Datalink layer
Unit of information
  Frame
Services
  Unreliable connectionless
  Reliable connection-oriented
Physical
Physical
Datalink
Datalink
Physical
Datalink
Frame
Protocols
  Ethernet
  Wi-Fi
  Bluetooth
  PPP

## Slide 11: Protocol stack Network layer
Unit of information
  packet
Services
  Unreliable connectionless
Organisation
  Datagram, virtual circuits
Physical
Physical
Datalink
Datalink
Network
Network
Physical
Datalink
Network
Packet
Protocols
  IPv4
  IPv6

## Slide 12: Protocol stack Transport layer
Unit of information
  segment
Services
  Unreliable connectionless
  Reliable connection-oriented
Physical
Physical
Datalink
Datalink
Network
Network
Physical
Datalink
Network
Transport
Transport
Segment
Protocols
  TCP
  UDP

## Slide 13: Protocol stack Application layer
Application layer protocols
  HTTP, SMTP, SSH, TLS, POP, IMAP, NTP, …
Physical
Physical
Datalink
Datalink
Network
Network
Physical
Datalink
Network
Transport
Transport
Application
Application
SDU
Layer1
Layer2
Layer3
Layer4

## Slide 14: OSI (seven layers) Reference Model
Physical
Physical
Datalink
Datalink
Network
Network
Physical
Datalink
Network
Transport
Transport
Application
Application
SDU
Session
Session
Presentation
Presentation
Layer7

## Slide 15: QUIC in the protocol stack
Physical layer (radio, fiber, cable, …)
Datalink layer (Ethernet, Wi-Fi, …)
Network layer (IPv4, IPv6)
Transport TCP
Transport (UDP)
TLS
HTTP/2
HTTP/3
QUIC

## Slide 16: First principle : QUIC frames
A QUIC packet contains
  a QUIC header
  one or more frames identified by a type field
QUIC frames can carry data and control information
  Easier to extend than the simple TCP header

## Slide 17: Simplified QUIC connection establishment
Basically a four-way handshake with Diffie Hellman to negotiate key
Initial (CRYPTO)
Initial (CRYPTO)
Handshake(CRYPTO)
Handshake (CRYPTO)
Handshake_Done
TLS ClientHello
Param negotiation
Clear text
TLS ServerHello
DH key known
TLS Encrypted Extensions
Certificate
TLS Finished
TLS established for server

## Slide 18: The QUIC Initial frame
Why is this packet so long ?
?

## Slide 19: Constraint on the Initial packet sent by client
Must contain at least 1200 bytes
  To be compared with TCP’s 40 bytes SYN over IPv4
Why forcing QUIC to send such a large initial packet ?
  This goes against a fast connection establishment
One way to counter reflection attacks
  Servers are not allowed to reply with more than 3 times the length of the initial client packet
  Also allows to verify that packets containing 1200 bytes can pass without any problem from client to server

## Slide 20: Protection against spoofed Initial packets
How can a QUIC server be protected against attacks using spoofed Initial packets ?
  Amplification factor of 3, sometimes more with some servers that use a certificate longer than three packets
?

## Slide 21: Protection against spoofed addresses
Initial (CRYPTO)
Initial (CRYPTO)
Handshake(CRYPTO)
Handshake (CRYPTO)
Handshake_Done
Client address unknown
TLSServerHello
DH key known
Certificate
TLS Encrypted Extensions
TLS Finished
TLS established for server
Retry (Token)
Initial (CRYPTO) + Token
Token valid
No state !
Is this the Retry token safer than TCP SYN cookies ?

## Slide 22: Second principle identifying QUIC connections
How to identify a QUIC connection ?
  Using the Source IP addresses and port numbers
Fragile if there are NATs
[SCID=x,DCID=z]
Initial (CRYPTO)
[SCID=y, DCID=x]
Initial (CRYPTO)
QUIC uses its own Connection-IDs
  QUIC enables the client and the server to use CIDs of different lengths
Client selects unique
CID x to identify connection
Server selects unique
CID y to identify connection
What is the size of the QUIC CID ?

## Slide 23: Negotiating options
How to negotiate options or QUIC extensions ?
[SCID=y, DCID=x]
Initial (CRYPTO)
Handshake(CRYPTO)
[SCID=x,DCID=z]
Initial (CRYPTO)
Client proposes transport parameters in Initial frame
Server selects agreed transport parameters in TLS Encrypted Extension

## Slide 24: The first Initial packet is not sent in clear
In TLS1.3, the ClientHello is sent in clear over the TCP connection
  Firewalls can observe the content of the ClientHello
QUIC wants to avoids as much as possible interference from firewalls and other types of middleboxes
The Initial packets are encrypted using a secret derived from the destination CID of the client’s Initial packet
Can wireshark decode an encrypted Initial ?

## Slide 25: Third principle : QUIC variable length header
How to represent a TCP header ?
  Textual representation

## Slide 26: The (long) QUIC header
Only used in the Initial, Retry and Handshake packets
One byte to indicate packet type and subtypes
32bits for version number !
Variable length CIDs

## Slide 27: Fourth principle: unique packet numbers
Each QUIC packet contains a unique packet number
If a packet is lost and needs to be retransmitted, the frames contained in the original packet will be copied in a new packet with a new packet number
On a QUIC connection, we never observe twice a packet with the same packet number !

## Slide 28: Encoding QUIC packet numbers
What is the length in bits of the QUIC packet numbers ?
  Use 8 bits
    Low overhead, but too short for many connections
  Use 16 bits
    Medium overhead, but too short for long transferts
  Use 32 bits
    Too short for very long transferts
  Use 64 bits
    Packet numbers are unlikely to be reused
    But this increases the per-packet overhead a lot
QUIC uses variable-length packet numbers to minimize overhead

## Slide 29: QUIC’s varint
A method to encoded variable length integers using bytes
Two high order bits of the bytestring indicate the length
  00: a one-byte long varint – from 0 to 26-1
  01: a two bytes long varint
  10: a four-bytes long varint
  11: an eigth-bytes long varint - from 0 to 262-1
All QUIC packet numbers are encoded as varints

## Slide 30: The (short) QUIC header
Used in all packets after the initial handshake
Type byte
The receiver knows the length of the CID it uses
varint
The frames that compose the packet

## Slide 31: The roles of the Connection identifier
On the server
  Identifies the corresponding QUIC connection
    A server may support thousands of connections at the same time
  Some servers are behind load balancers
    Load balancer distributes load based on CID of incoming packets
On the client
  The client supports a small number of QUIC connections
  Each connection can be identified using the UDP port numbers and IP addresses
Some QUIC clients use zero-length CIDs
  Server does not send CIDs in the returned packets
LB

## Slide 32: How to close a QUIC connection ?
Implicit termination
  During connection establishment, client and server exchange the max_idle_timeout parameter (in seconds)
  Connection is closed if it has been idle for this duration
Explicit termination
  Host sends CONNECTION_CLOSE frame to indicate the abrupt termination of a QUIC connection
Graceful termination
  Part of the data exchange

## Slide 33: Exchanging data during the handshake ?
To reduce latency, is it possible to exchange data during the handshake ?
  Yes, provided that the client and the server have agreed on security keys which they can use to encrypt the data during the handshake
    Pre-shared key
    TLS session ticket containing the keys from a previous QUIC connection

## Slide 34: 0-RTT packets
Can be sent during the handshake to exchange data
[SCID=x, DCID=y]
Initial (CRYPTO)
Handshake(CRYPTO)
[SCID=x,DCID=z]
Initial (CRYPTO) 0-RTT(Data)
Encrypted using previous TLS ticket

## Slide 35: Replays and 0-RTT packets
QUIC cannot guarantee that 0-RTT data will be delivered only ONCE to a server
An application that uses QUIC’s 0-RTT must ensure that the data sent in 0-RT is idempotent and can be replayed without any problem
[SCID=x, DCID=y]
Initial (CRYPTO)
Handshake(CRYPTO)
[SCID=x,DCID=z]
Initial (CRYPTO) 0-RTT(Data)
[SCID=x,DCID=z]
Initial (CRYPTO) 0-RTT(Data)

## Slide 36: QUIC allows to multiplex several bytestreams on a single connection
What is the information required in each STREAM frame to support this feature ?
?

## Slide 37: Transporting data streams
QUIC defines several types of frames to reliably exchange data
  STREAM frame

## Slide 38: The STREAM frame
0001XYZF
FIN bit indicates end of STREAM
Indicates whether Offset and length are present
Each bytestream has a unique identifer
Offset in bytes from beginning of bytestream
Length of frame in bytes
All integers are varint

## Slide 39: Example
Client sends ABCDEFG over STREAM 1 and 123 over STREAM 5
PN = 1
AB
1
C
DEFG
23
PN = 2
PN = 3
PN = 4

## Slide 40: The stream identifiers
Each bytestream has a unique identifier, but who allocates thes identifiers ?
  The client
  The server
  Both
    Risk of collision
To prevent collisions, the low order bits of the stream identifier indicate the host that is responsible for the stream identifiers
  00 : bidirectional stream identifier created by client
  10 : unidirectional stream identifier created by client
  01 : bidirectional stream identifier created by server
  11 : unidirectional stream identifier created by server

## Slide 41: Acknowledging QUIC packets
A QUIC receiver always acknowledges the received packets
Not the individual frames (the sender must remember in which packet each frame was sent)
  How would you design the QUIC ACK frame
?

## Slide 42: QUIC loss detection
How to detect packet losses ?
  Sender always uses monotonically increasing packet numbers
    Initial packet number may start at another value than zero
    Sender can decide to create gaps in packet number if it wants
  Receiver acknowledges QUIC packets using ACK frames
    Packets containing only ACK, PADDING and CONNECTION_CLOSE frames do not need to be acked
Largest QUIC PN received
Similar to TCP’s SACK blocks

## Slide 43: QUIC ack delays
QUIC needs to accurately measure round-trip-times like TCP
But a QUIC receiver may not always send an ACK for each received packet
  Standard requires sending one ACK every two packets, but implementations vary
  Some implementations delay the transmission of ACK frames
PN=9
ACK[L=5, Delay=d]
PN=3
PN=5
PN=4
d
Rtt= ?
t3
t4
t5
ta
Rtt=ta- t5-d

## Slide 44: Closing bytestreams
How to close bytestreams ?
  Gracefully
    Sender sets the FIN bit in the STREAM frame containing the last byte of the stream
  Abruptly by the sender
    Sender sends a RESET_STREAM frame whose parameter is the identifier of the stream being closed
  Abruptly by the receiver
    Receiver sends a STOP_SENDING frame to indicate that it discards all data for a given bytestream

## Slide 45: QUIC flow control
QUIC supports different levels of flow control
Connection level
  When the connection starts, a receiver indicates the maximum amount of data that it accepts with initial_max_data transport parameter
  During the connection, it can adjust this limit with the MAX_DATA frame
Number of streams
  Initial_max_streams_bidi and Initial_max_streams_uni transport parameters exchanged during the handshake
  MAX_STREAMS frame can be used to adjust this limit during the connection

## Slide 46: QUIC flow control
At the stream level
  Transport parameters allow to specify the maximum number on bytes which can be received on a stream
  MAX_STREAM_DATA allows to adjust this limit on a given stream during the connection
When a sender is blocked by the flow control imposed by a receiver, it should send a DATA_BLOCKED or STREAM_DATA_BLOCKED to inform the receiver and encourage it to adjust the limits
  These control frames are acknowledged and retransmitted if lost to prevent the window-zero problems that affect TCP

## Slide 47: TLS/TCP and QUIC security
Attacker is on-path but does not know security keys, it can change
  Information inside payload
    Inject new data in payload
  Information inside TCP header
    Generate new TCP segments for a connection
TLS records
[encrypted and authenticated]
How can these protocols cope with on-path attackers that are able to observe packets and send spoofed packets ?
What kind of attacks are prevented by using TLS over TCP ?

## Slide 48: Some on-path attacks
TCP RST attack
  Attacker breaks an established TCP connection by sending a spoofed RST
  When receiving a RST segment, receiver checks that it contains a valid sequence number
    If yes, the TCP connection is terminated
TCP injection attack
  Attacker injects new TCP segment with a specific payload
    Attacker can easily determine the sequence numbers to use in TCP header
    Attacker does not know security keys, receiver will reject incoming TLS records and stop the TLS session

## Slide 49: How to improve the resilience TCP against such attacks ?
We also need to protect the TCP header
  Encrypt TCP header
    Would break many middleboxes like firewals that inspect the TCP header
  Authenticate the TCP header
    Possible with the TCP-AO option, but requires security keys that usually need to be manually configured
https://datatracker.ietf.org/doc/html/rfc5925

## Slide 50: Fifth principle: Encrypt and authenticate most of QUIC packets
Sent as clear text Visible by routers, NATs, firewalls
Encrypted and authenticated using connection keys
On-path attackers cannot even observe QUIC packet numbers !

## Slide 51: QUIC and malformed packets
What happens if attacker modifies a packet on a QUIC connection ?
Packet reception
  QUIC receiver verifies the integrity of the packet using the authentication
    If packet fails this check, it is discarded
  QUIC receivers decrypts the contents of the packet
    It can then access the packet number and the frames contained in the packet
On-path attackers cannot break an established QUIC connection by injecting packets or modifying packets sent over this connection

## Slide 52: Exchanging datagrams
Can we use QUIC to carry datagrams (e.g. Voice over IP) ?
  The STREAM frames are always acknowledged and retransmitted if needed
Negotiate DATAGRAM extension during handshake
  Client proposes max_datagram_frame_size > 0
  Server selects value if supported
New DATAGRAM frame
  DATAGRAM frames are NOT retransmitted
  But packets carrying these frames are acknowledged
Low order bit indicates if Length field is present

## Slide 53: QUIC connection migration
Smartphone would like to migrate established QUIC connections to cellular when losing Wi-Fi and vice-versa
First approach
  Smartphone has two IP addresses and uses them at will
S=IPS, D=IP1
1-RTT(…)
S=IP1,D=IPS, DCID=123
1-RTT(Data)
IP1
Cell
IP2
Wi-Fi
S=IP2,D=IPS, DCID=123
1-RTT(Data)
S=IPS, D=IP2
1-RTT(…)
How secure is this approach ?
IPS
Server

## Slide 54: QUIC connection migration
Principle
  Server allocates several connection identifiers to each client
  If a client needs to use a different path to reach the server, it must use a new connection identifier
S=IPS, D=IP1
1-RTT(…)
S=IP1,D=IPS, DCID=123
1-RTT(Data)
IP1
Cell
IP2
Wi-Fi
S=IP2,D=IPS, DCID=456
1-RTT(PATH_CHAL(x))
S=IPS, D=IP2
1-RTT(PATH_RESP(x), PATH_CHAL(y))
IPS
Server
Other CID: 456
S=IP2,D=IPS, DCID=456
1-RTT(PATH_RESP(y))
How can the server validate the client ?

## Slide 55: QUIC extensions