## Slide 1: Part 7 Building a network

## Slide 2
https://adv-net.ethz.ch/transcripts/

## Slide 3: Agenda
Building a network
  Virtual circuit organization
  Datagram organization
  Static routing
  Distance vector routing
  Link state routing

## Slide 4: How to transfert information ?
Divide it in small blocks called packets which can be sent independently
ABCDEFGHIJKLMNOPQRSTUVWXYZ1234
ABCDEFGHIJKLM
NOPQRSTUVW
XYZ1234

## Slide 5: How to organise a network ?
Source: wikipedia : https://en.wikipedia.org/wiki/Post_office and https://en.wikipedia.org/wiki/Telephone_exchange

## Slide 6: Agenda
Building a network
  Virtual circuit organisation
  Datagram organisation
  Static routing
  Distance vector routing
  Link state routing

## Slide 7: Virtual circuit
Basic idea
  Create circuits through the network to transfer data divided in packets
  Packets contain one (or more) labels
  Simpler forwarding table
    incoming label, nexthop, outgoing label

## Slide 8: Virtual circuit
B
A
R1
R2
R3
C
3 -> 5, South East
2 -> 3, South East
1 -> 2, North East
5 -> 2, South East
3 -> 1, South East
3
1

## Slide 9: Agenda
Building a network
  Virtual circuit organisation
  Datagram organisation
  Static routing
  Distance vector routing
  Link state routing

## Slide 10: Datagram organisation
Principles
  Two types of devices
    Hosts
    Routers
  Packet
    Source and destination addresses

## Slide 11: Datagram mode
Early work on this concept that led to the current Internet was done in France
Cyclades project lead by Louis Pouzin
http://goo.gl/lwdlwS

## Slide 12: A network
B
A
R1
R2
R3
Contents of the forwarding table
  Destination, nexthop/outgoing if
A: West
B: East
A: North
B: North-East
A: North
B: South-East

## Slide 13: How to compute the forwarding tables ?
A simple solution: Port-station table
  When a node boots, its forwarding table is empty, is it possible to learn automatically the forwarding table from the data packets ?

## Slide 14: Another network
B
A
R1
R2
R3

## Slide 15: A simple network
B
A
R1
R2
R3
A->B
A: West
A->B
A->B
A: North
A->B
A: North-West
B->A
B->A
B->A

## Slide 16: Another network
B
A
R1
R2
R3
B: S-E
B: East
B: South
B->A
B->A
B->A
B->A
B->A
B->A
B: North
B: S-W
B->A
The port-station table can only be used in tree-shaped networks !

## Slide 17: Source routing
Basic idea
  Each node has a unique address
  Each node knows its direct neighbors
    How ?
  Each packet contains the list of the addresses of intermediate nodes

## Slide 18: Source routing (2)
B
A
R1
R2
R3
A: West
R2: South-West
R3: East
R1: North
R2: North-East
B: South
R1: North-West
R2: South-West
A->B via R1,R3
A->B via R1,R3
A->B via R1,R3
B->A via R3,R2,R1
B->A via R3,R2,R1
B->A via R3,R2,R1

## Slide 19: Can we do better ?
Networks must be redundant to cope with failures
  tree-shaped networks are not sufficient
Source routing consummes header space

## Slide 20: Agenda
Building a network
  Virtual circuit organisation
  Datagram organisation
  Static routing
  Distance vector routing
  Link state routing

## Slide 21: Static routing
Compute forwarding tables for all nodes such that all nodes can send packets to any other nodes in the network
C
E
A
B
C
D
E
Paths to C
Paths to A

## Slide 22: Static routing
What are the criterias that must be fulfilled ?
?
  Each node must have at least one path towards each other node
    No blackhole
  The set of paths towards a given destination must form an acyclic graph
    No forwarding loop

## Slide 23: Static routing
C
E
A
B
C
D
E
Routing table
A : Local
D : South
B : East
C : East [via B]
E: East [via B]
Routing table
A : South
B : Local
C : East
E : South
Routing table
A : West [via B]
B : West
C : Local
D : West [via B]
E : South West
Routing table
A : East [via E]
B : North [via A]
C : East [via E]
D : Local
E : East
Routing table
A : West [via D]
B : North
C : North-East
D : West
E : Local
Is this set of forwarding tables valid ?
Paths to D
Paths to A
Paths to E

## Slide 24: Static routing
C
E
A
B
C
D
E
Routing table
A : Local
D : South
B : East
C : East [via B]
E: East [via B]
Routing table
A : West
B : Local
C : East
D : South [via E]
E : South
Routing table
A : West [via B]
B : West
C : Local
D : West [via B]
E : South West
Routing table
A : North
B : North [via A]
C : East [via E]
D : Local
E : East
Routing table
A : North [via B]
B : North
C : North-East
D : West
E : Local
Is this set of forwarding tables valid ?
Paths to E
Paths to D
Paths to A

## Slide 25: Static routing in practice
Forwarding tables are often computed based on a weighted graph along shortest paths
C
E
A
B
C
D
E
Routing table
A : Local
D : East [via B]
B : East
C : East [via B]
E: East [via B]
Routing table
A : West
B : Local
C : East
D : South [via E]
E : South
Routing table
A : West [via B]
B : West
C : Local
D : S-West [via E]
E : South West
Routing table
A : East [via E]
B : East [via E]
C : East [via E]
D : Local
E : East
Routing table
A : North [via B]
B : North
C : North-East
D : West
E : Local
2
2
2
5
1
1
3
3

## Slide 26: Question
C
E
A
B
C
D
E
Routing table
A : Local
D : South
B : East
C : East [via B]
E: East [via B]
Routing table
A : West
B : Local
C : East
D : South [via E]
E : South
Routing table
A : West [via B]
B : West
C : Local
D : West [via B]
E : South West
Routing table
A : North
B : North [via A]
C : East [via E]
D : Local
E : East
Routing table
A : North [via B]
B : North
C : North-East
D : West
E : Local
Link A-B fails, which tables must be updated ?

## Slide 27: Allocating addresses in IP networks
Example
  Allocate 192.0.2.0/24 (256 addresses)
R1
R2
R3
192.0.2.0/26
192.0.2.64/26
192.0.2.128/26
192.0.2.192/26
10.0.0.1/31
10.0.0.0/31
10.0.0.2/31
10.0.0.3/31
10.0.0.4/31
10.0.0.5/31

## Slide 28: IPv4 subnets
An IPv4 subnet is a group of IPv4 addresses that have the same prefix (high order n bits)
Examples
  2.3.4.0/24 means 2.3.4.0 -> 2.3.4.255
  3.4.5.128/25 means 3.4.5.128 -> 3.4.5.255
  4.5.6.64/27 means 4.5.6.64 -> 4.5.6.95
What is the last address of the 5.6.7.32/29 ?

## Slide 29: Allocating addresses
IPv6 campus network
  2001:db8:1234::/48
2001:db8:1234:A::/52
2001:db8:1234:B::/52
2001:db8:1234:C::/52
2001:db8:1234:11::/56

## Slide 30: Allocating addresses
Inside a campus
  2001:db8:1234:A::/52
  2001:db8:1234:A0::/54
  2001:db8:1234:A0::/54
  2001:db8:1234:A4::/54
  2001:db8:1234:A8::/53
  2001:db8:1234:AA::/55
  2001:db8:1234:A8::/55
  2001:db8:1234:AC::/55
  2001:db8:1234:AE::/55

## Slide 31: Packet forwarding on IPv4 routers
When an IPv4 router forwards an IPv4 packet, it always uses longest prefix match
Destination Gateway
0.0.0.0/0 192.168.0.1
127.0.0.1 lo0
130.104.0.0/16 192.168.0.2
130.104.12.128/26 192.168.0.3
130.104.12.192/27 192.168.0.4
192.168.0.0/24 eth0
Packets to 130.105.12.194, 130.104.12.176 130.104.12.254,

## Slide 32: Packet forwarding on IPv6 routers
When an IPv6 router forwards an IPv6 packet, it always uses longest prefix match
Destination Gateway
::/0 fe80::dead:beef
::1 ::1
2a02:2788:2c4:16f::/64 eth0
2001:6a8:3080::/48 fe80::bad:cafe
2001:6a8:2d80::/48 fe80::bad:bad
2001:6a8::/32 fe80::aaaa:bbbb
Packets to 2001:6a8:3080::1234, 2001:2788:123a::1:1e, 2001:6a8:3880:40::2

## Slide 33: Example
A’s routing table
destination interface/NH
::/0 2001:db8:7::B
2001:db8:7/48 2001:db8:4::C
2001:db8:1/48 West
2001:db8:4/48 East
2001:db8:7/48 North
B’s routing table
destination interface/NH
::/0 2001:db8:5::C 2001:db8:2/47 2001:db8:6::E 2001:db8:5/48 South 2001:db8:6/48 East
2001:db8:7/48 West
C’s routing table
destination interface/NH
2001:db8:1/48 2001:db8:5::B
2001:db8:2/47 2001:db8:3::E
2001:db8:2/48 2001:db8:5::B
2001:db8:3/48 East
2001:db8:4/48 West
2001:db8:5/48 North
2001:db8:6/47 2001:db8:5::B
E’s routing table
destination interface/NH
::/0 2001:db8:6::B
2001:db8:2/48 East 2001:db8:3/48 West 2001:db8:6/48 North
RA
RB
RC
RE
2001:db8:1/48
2001:db8:7/48
2001:db8:6/48
2001:db8:5/48
2001:db8:4/48
2001:db8:3/48
2001:db8:2/48
RA
RB
RC
RE

## Slide 34: Agenda
Building a network
  Virtual circuit organisation
  Datagram organisation
  Static routing
  Distance vector routing
  Link state routing

## Slide 35: Dynamic routing protocols
Objective
  Develop a distributed algorithm that automatically computes the routing tables of all routers in a network
  Each router is configured with its addresses and a cost is associated to each directed link

## Slide 36: Computing forwarding tables
How to compute the forwarding tables for all routers in a network ?
C
E
A
B
C
D
E
dest -> interface

## Slide 37: Computing forwarding tables
C
E
A
B
C
D
E
Routing table
A : Local
D : South
B : East
C : East [via B]
E: East [via B]
Routing table
A : West
B : Local
C : East
D : South [via E]
E : South
Routing table
A : West [via B]
B : West
C : Local
D : West [via B]
E : South West
Routing table
A : North
B : North [via A]
C : East [via E]
D : Local
E : East
Routing table
A : North [via B]
B : North
C : North-East
D : West
E : Local
Cost=1
Cost=1
Cost=1
Cost=1
Cost=1
Cost=1

## Slide 38: Distance vector routing
Objectives of the routing protocol
  Automatically compute all forwarding tables so that each node can reach any node in the network with a loop-free path
Principle
  Each node regularly sends a summary of its forwarding table to its neighbors

## Slide 39: Distance vector
C
D
E
Routing table
A : 0 [ Local ]
A
B
C
D
E
Routing table
B : 0 [Local]
Routing table
C : 0 [Local]
Routing table
E : 0 [Local]
Routing table
D : 0 [Local]
Cost=1
Cost=1
Cost=1
Cost=1
Cost=1
Cost=1

## Slide 40: Distance vector example (2)
C
D
E
Routing table
A : 0 [ Local ]
A
B
C
D
E
Routing table
B : 0 [Local]
A : 1 [West]
Routing table
C : 0 [Local]
Routing table
E : 0 [Local]
Routing table
D : 0 [Local]
A : 1 [North]
D=0 ; A=1
D=0 ; A=1

## Slide 41: Distance vector example (3)
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
A
B
C
D
E
Routing table
B : 0 [Local]
A : 1 [West]
Routing table
C : 0 [Local]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
Routing table
D : 0 [Local]
A : 1 [North]
C=0
C=0

## Slide 42: Distance vector example (4)
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
A
B
C
D
E
Routing table
B : 0 [Local]
A : 1 [West]
C : 1 [East]
Routing table
C : 0 [Local]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
Routing table
D : 0 [Local]
A : 1 [North]
E=0;D=1;A=2;C=1
E=0;D=1;A=2;C=1
E=0;D=1;A=2;C=1

## Slide 43: Distance vector example (5)
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
A
B
C
D
E
Routing table
B : 0 [Local]
A : 1 [West]
C : 1 [East]
E : 1 [South]
D : 2 [South]
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A : 3 [South-West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B=0;A=1;C=1;D=2;E=1
B=0;A=1;C=1;D=2;E=1

## Slide 44: Distance vector example (6)
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : 1 [East]
C : 2 [East]
E : 2 [East]
A
B
C
D
E
Routing table
B : 0 [Local]
A : 1 [West]
C : 1 [East]
E : 1 [South]
D : 2 [South]
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A : 2 [West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
A=0;B=1;C=2;D=1;E=2

## Slide 45: Distance vector example (7)
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : 1 [East]
C : 2 [East]
E : 2 [East]
A
B
C
D
E
Routing table
B : 0 [Local]
A : 1 [West]
C : 1 [East]
E : 1 [South]
D : 2 [South]
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A : 2 [West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : 2 [North]

## Slide 46: What is the distance vector sent by R5 after convergence ?
R1
R2
R3
R4
R5
R6
4
4
10
9
1
1
1
1

## Slide 47: Distance vectors
  How to deal with link failures ?
C
D
E
A
B
C
D
E

## Slide 48: How to react ?
All routes that use a failed link are advertised with an infinite cost
Routing table
A : 0 [ Local ]
D : 1 [South]
B : ∞
C : ∞
E : ∞
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A : 2 [West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : 2 [North]
A=0;B=∞;C=∞;D=1;E=∞
Routing table
B : 0 [Local]
A : ∞
C : 1 [East]
E : 1 [South]
D : 2 [South]

## Slide 49: Question
  How does a router using distance vectors detect the failure of a link ?

## Slide 50: DV sent by R4 when link fails ?
R1
R2
R3
R4
R5
R6
3
4
10
9
Default link weight is 1

## Slide 51: Student question
What is the difference between a routing table and a forwarding table ?

## Slide 52: Question
A distance vector router accepts a route towards destination d on link l if any of three conditions is met. What are these three conditions ?
  d is not already in the routing table
  d is already in the routing table, but with a shorter path
  d is already in the routing table, but with a longer path
  the sequence number of the distance vector is larger than the previous one
  d is already in the routing table, but the route was learned from another link than l
  d is already in the routing table, and the route was learned on link l

## Slide 53: Reception of DV
Received(Vector V[],link l)
{ /* received vector from link l */
for each destination=d in V[]
{
if (d isin R[])
{ if ( ((V[d].cost+l.cost) < R[d].cost) OR ( R[d].link == l) )
{ /* better route or change to current route */
R[d].cost=V[d].cost+l.cost;
R[d].link=l;
}
}
else
{ /* new route */
R[d].cost=V[d].cost+l.cost;
R[d].link=l;
}
}

## Slide 54: Example
    D must remove all the routes learned from North that are announced with an ∞ cost
Routing table
A : 0 [ Local ]
D : 1 [South]
B : ∞
C : ∞
E : ∞
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A : 2 [West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : 2 [North]
A=0;B=∞;C=∞;D=1;E=∞
Routing table
B : 0 [Local]
A : ∞
C : 1 [East]
E : 1 [South]
D : 2 [South]

## Slide 55: Example
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : ∞
C : ∞
E : ∞
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A : 2 [West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : ∞
D=0;B= ∞;A=1;C=2;E=11
Routing table
B : 0 [Local]
A : ∞
C : 1 [East]
E : 1 [South]
D : 2 [South]

## Slide 56: Example
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : ∞
C : 3 [South]
E : 2 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A : 2 [West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : ∞
Routing table
B : 0 [Local]
A : ∞
C : 1 [East]
E : 1 [South]
D : 2 [South]
B=0;A=∞;C=1;E=1;D=2
B=0;A=∞;C=1;E=1;D=2

## Slide 57: Example
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : ∞
C : 3 [South]
E : 2 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A : ∞∞
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : ∞
Routing table
B : 0 [Local]
A : ∞
C : 1 [East]
E : 1 [South]
D : 2 [South]
E=0;A=2;D=1;C=1;B=1
E=0;A=2;D=1;C=1;B=1
E=0;A=2;D=1;C=1;B=1

## Slide 58: Example
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : ∞
C : 3 [South]
E : 2 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A: 3 [South-West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : 2 [East]
Routing table
B : 0 [Local]
A : 3 [South]
C : 1 [East]
E : 1 [South]
D : 2 [South]
A=1;B=2;C=2;D=1;E=1
    Everything is ok ?

## Slide 59: Another failure
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : 3 [South]
C : 3 [South]
E : 2 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A: 3 [South-West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : 2 [East]
Routing table
B : 0 [Local]
A : 3 [South]
C : 1 [East]
E : 1 [South]
D : 2 [South]
A=1;B=∞;C=∞;D=1;E=∞

## Slide 60: Another failure
  But A could also send its distance vector before D
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : 3 [South]
C : 3 [South]
E : 2 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A: 3 [South-West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : ∞
C : ∞
B : ∞
Routing table
B : 0 [Local]
A : 3 [South]
C : 1 [East]
E : 1 [South]
D : 2 [South]
A=0;D=1;B=3;C=3;E=2

## Slide 61: Another failure
    D updates its routing table
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : 3 [South]
C : 3 [South]
E : 2 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A: 3 [South-West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 3 [North]
C : 4 [North]
B : 4 [North]
Routing table
B : 0 [Local]
A : 3 [South]
C : 1 [East]
E : 1 [South]
D : 2 [South]
D=0;A=1;E=3;C=4;B=4

## Slide 62: Another failure
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : 5 [South]
C : 5 [South]
E : 4 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A: 3 [South-West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 3 [North]
C : 4 [North]
B : 4 [North]
Routing table
B : 0 [Local]
A : 3 [South]
C : 1 [East]
E : 1 [South]
D : 2 [South]
A=0;D=1;B=5;C=5;E=4

## Slide 63: Another failure
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : 5 [South]
C : 5 [South]
E : 4 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A: 3 [South-West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 5[North]
C : 6 [North]
B : 6 [North]
Routing table
B : 0 [Local]
A : 3 [South]
C : 1 [East]
E : 1 [South]
D : 2 [South]
A=1;D=0;B=6;C=6;E=5
This problem is called counting to infinity
  How can we prevent it ?

## Slide 64: Preventing count to infinity
Split horizon
Split horizon with poisoning
Notes: Pseudocode
Every N seconds:
for each link=l
{ /* one different vector for each link */
Vector=null;
for each destination=d in R[]
{
if (R[d].link<>l)
{
Vector=Vector+Pair(d,R[d].cost);
}
}
Send(Vector);
}

## Slide 65: Agenda
Building a network
  Datagram organisation
  Virtual circuit organisation
  Static routing
  Distance vector routing
  Link state routing

## Slide 66: Link state routing
Objectives of the routing protocol
  Compute all forwarding tables
Principle
  Each node detects its direct neighbors
  Each node regularly sends the list of its direct neighbors to all nodes

## Slide 67: Discovering neighbours
Manually
Automatically
E
A
B
E
B:HELLO
A:HELLO
E:HELLO

## Slide 68: Link state packets
How to reliably send LSPs to all nodes ?
C
D
E
Links
A-B : 1
A-D : 1
A
B
C
D
E
Links
B-C : 1
C-E : 1
Links
E-D : 1
E-B : 1
E-C : 1
Links
A-D : 1
D-E : 1
Links
A-B : 1
B-E : 1
B-C : 1
Links
A-D : 1
D-E : 1
LSP : E [D:1];[B:1];[C:1]
LSP : E [D:1];[B:1];[C:1]
LSP : E [D:1];[B:1];[C:1]

## Slide 69: Distributing LSPs
Naive approach
  Forward received LSP to all neighbors
C
D
E
Links
A-B : 1
A-D : 1
A
B
C
D
E
Links
B-C : 1
C-E : 1
B-E : 1
D-E : 1
Links
E-D : 1
E-B : 1
E-C : 1
Links
A-B : 1
B-E : 1
B-C : 1
E-D : 1
E-C : 1
Links
A-D : 1
D-E : 1
B-E : 1
E-C : 1
LSP : E [D:1];[B:1];[C:1]
LSP : E [D:1];[B:1];[C:1]
LSP : E [D:1];[B:1];[C:1]
With this approach, LSPs will loop forever...

## Slide 70: Flooding
C
D
E
Links
A-B : 1
A-D : 1
A
B
C
D
E
Links
B-C : 1
C-E : 1
Links
E-D : 1
E-B : 1
E-C : 1
Links
A-D : 1
D-E : 1
Links
A-B : 1
B-E : 1
B-C : 1
Links
A-D : 1
D-E : 1
LSP : E-0 [D:1];[B:1];[C:1]
LSP : E-0 [D:1];[B:1];[C:1]
LSP : E-0 [D:1];[B:1];[C:1]
LSPs
LSPs
LSPs
E-0 [D:1];[B:1];[C:1]
LSPs
LSPs
New LSP, flood !
New LSP, flood !
New LSP, flood !

## Slide 71: Flooding
C
D
E
Links
A-B : 1
A-D : 1
A
B
C
D
E
Links
B-C : 1
C-E : 1
B-E : 1
D-E : 1
Links
E-D : 1
E-B : 1
E-C : 1
Links
A-B : 1
B-E : 1
B-C : 1
E-D : 1
E-C : 1
Links
A-D : 1
D-E : 1
B-E : 1
E-C : 1
LSP : E-0 [D:1];[B:1];[C:1]
LSP : E-0 [D:1];[B:1];[C:1]
LSPs
E-0 [D:1];[B:1];[C:1]
LSPs
E-0 [D:1];[B:1];[C:1]
LSPs
E-0 [D:1];[B:1];[C:1]
LSPs
E-0 [D:1];[B:1];[C:1]
LSPs
LSP : E-0 [D:1];[B:1];[C:1]
A already knows E-0
C already knows E-0

## Slide 72: After flooding
Each node knows full network topology
  computes shortest paths from graph
C
D
E
A
B
C
D
E
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Paths to D
Paths to A
Paths to E

## Slide 73: Summary
Building a network
  Datagrams and Virtual Circuits
Static routing
  Longest match packet forwarding in IP
Dynamic routing protocols
  Distance Vector, Link State