## Slide 1: Part 8 Routing protocols

## Slide 2: Agenda
Routing protocols
  Distance Vector routing
  Link state routing
Routing in IP networks
Interdomain routing

## Slide 3: Question
A distance vector router accepts a route towards destination d on link l if any of three conditions is met. What are these three conditions ?
  1. d is not already in the routing table
  2. d is already in the routing table, but with a shorter path
  3. d is already in the routing table, but with a longer path
  4. the sequence number of the distance vector is larger than the previous one
  5. d is already in the routing table, but the route was learned from another link than l
  6. d is already in the routing table, and the route was learned on link l

## Slide 4: Reception of DV
Received(Vector V[],link l)
{ /* received vector from link l */
for each destination=d in V[]
{
if (d isin R[])
{ if ( ((V[d].cost+l.cost) < R[d].cost) OR ( R[d].link == l) )
{ /* better route or change to current route */
R[d].cost=V[d].cost+l.cost;
R[d].link=l;
}
}
else
{ /* new route */
R[d].cost=V[d].cost+l.cost;
R[d].link=l;
}
}

## Slide 5: DV sent by R3 to R1 with split horizon?
R1
R2
R3
R4
R5
R6
3
4
10
9
Default link weight is 1

## Slide 6: Split horizon
  A will not pollute D’s routing table
E
Routing table
A : 0 [ Local ]
D : 1 [South]
B : 3 [South]
C : 3 [South]
E : 2 [South]
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A: 3 [South-West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : 1 [East]
C : 2 [East]
B : 2 [East]
Routing table
B : 0 [Local]
A : 3 [South]
C : 1 [East]
E : 1 [South]
D : 2 [South]
A=0

## Slide 7: Split horizon (2)
  D can also send its distance vector
C
D
E
Routing table
A : 0 [ Local ]
D : 1 [South]
E : ∞
C : ∞
B : ∞
A
B
C
D
E
Routing table
C : 0 [Local]
E : 1 [South-West]
D : 2 [South-West]
A: 3 [South-West]
B : 1 [West]
Routing table
E : 0 [Local]
D : 1 [West]
A : 2 [West]
C : 1 [North-East]
B : 1 [North]
Routing table
D : 0 [Local]
A : 1 [North]
E : ∞
C : ∞
B : ∞
Routing table
B : 0 [Local]
A : 3 [South]
C : 1 [East]
E : 1 [South]
D : 2 [South]
D=0;B=∞;C=∞;E=∞
Does split horizon allows to avoid all counting to infinity problems ?

## Slide 8: Limitations of split horizon with poisoning
C
E
Routing table
A : 0 [ Local ]
B : ∞ ∞
C : ∞ ∞
E : ∞ ∞
A
B
C
E
Routing table
C : 0 [Local]
E : 1 [South-West]
A : 2 [West]
B : 1 [West]
Routing table
E : 0 [Local]
A : 2 [North]
C : 1 [North-East]
B : 1 [North]
Routing table
B : 0 [Local]
A : 1 [West]
C : 1 [East]
E : 1 [South]
A=2;B=1; C=0;E=∞
A=∞;B=0; C=1;E=∞
A=∞;B=0; C=∞ E=1

## Slide 9: Limitations
    E will send its own distance vector
      B will discover a new route towards A via E and will advertise it to C
      New count to infinity problem
C
E
Routing table
A : 0 [ Local ]
B : ∞∞
C : ∞ ∞
E : ∞ ∞
A
B
C
E
Routing table
C : 0 [Local]
E : 1 [South-West]
A : 2 [West]
B : 1 [West]
Routing table after B’s vector
E : 0 [Local]
A : ∞
C : 1 [North-East]
B : 1 [North]
Routing table after C’s vector
E : 0 [local]
A : 3 [North-East]
C : 1 [North-East]
B : 1 [North]
Routing table
B : 0 [Local]
A : 1 [West]
C : 1 [East]
E : 1 [South]
A=∞;B=0; C=1;E=∞
A=2;B=1; C=0;E=∞

## Slide 10: Operational issue
Operation
  At each expiration of its 30-sec timer, each router sends its own distance vector and restarts its timer
Problem
  After a power failure, all routers might restart at same time and have synchronized timers
    Each router will need to process bursts of DV messages
See The Synchronization of Periodic Routing Messages , Floyd, S., and Jacobson, V. IEEE/ACM Transactions on Networking, V.2 N.2, p. 122-136, April 1994.
Notes: The Synchronization of Periodic Routing Messages , Floyd, S., and Jacobson, V. IEEE/ACM Transactions on Networking, V.2 N.2, p. 122-136, April 1994.

## Slide 11: Loop-free routing
What guarantees the fact that packets sent to destination d will eventually reach destination d ?

## Slide 12: Agenda
Routing protocols
  Distance Vector routing
  Link state routing
Routing in IP networks
Interdomain routing

## Slide 13: Question
Which of the following informations are contained in a link state packet ?
  1. sequence number
  2. list of paths to reach known destinations
  3. list of pairs (known dest, cost)
  4. age of the link state packet
  5. clock time
  6. list of pairs (neighbor, cost to this neighbor)
  7. CRC

## Slide 14: Link state packet sent by R4 ?
R1
R2
R3
R4
R5
R6
3
4
10
9
Default link weight is 1

## Slide 15: How to set link costs ?
By manual configuration
Based on link bandwidth
By measurements
Only strictly positive link weights

## Slide 16: What is the role of
Sequence number in link state packets
  How to deal with wrap around ?
Age field in link state packets
CRC in link state packets

## Slide 17: Two way connectivity check
C
D
E
A
B
C
D
E
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-1 [D:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
Links
A-B, B-A : 1
B-E, E-B : 1
B-C, C-B : 1
E-D, D-E : 1
E-C, C-E : 1
A-D, D-A : 1
LSPs
E-0 [D:1];[B:1];[C:1]
A-0 [D:1];[B:1]
B-0 [A:1] [C:1] [E:1]
C-0 [B:1] [E:1]
D-0 [A:1] [E:1]
LSP : E-1 [D:1];[C:1]
LSP : E-1 [D:1];[C:1]
A link is only considered useable only if both directions have been advertised

## Slide 18: Transient problems when a link fails
A
B
C
D
100
A's FIB
B : East
C : South
D : East
D's FIB
A : North
B : North
C : North
C's FIB
A : North
B : North
D : North
B's FIB
A : West
C : West
D : South
A and B are not yet aware of failure
Packets will be lost

## Slide 19: A detects the failure
A
B
C
D
100
A's FIB
B : East
C : South
D : East
D's FIB
A : North
B : North
C : North
C's FIB
A : North
B : North
D : North
B's FIB
A : West
C : West
D : South
B not yet aware of failure
A cannot reach B/D
Packets continue to be lost

## Slide 20: A recomputes Dijkstra and sends its LSP
A
B
C
D
100
A's FIB
B : South
C : South
D : South
D's FIB
A : North
B : North
C : North
C's FIB
A : North
B : North
D : North
B's FIB
A : West
C : West
D : South
B not yet aware of failure
A loops towards B/D
Packets continue to be lost
A:1 C=1

## Slide 21: B detects the failure
A
B
C
D
100
A's FIB
B : South
C : South
D : South
D's FIB
A : North
B : North
C : North
C's FIB
A : North
B : North
D : North
B's FIB
A : West
C : West
D : South
B cannot reach A/C
A loops towards B/D
Packets continue to be lost
A:1 C=1

## Slide 22: B recomputes Dijkstra and sends its LSP
A
B
C
D
100
A's FIB
B : South
C : South
D : South
D's FIB
A : North
B : North
C : North
C's FIB
A : North
B : North
D : North
B's FIB
A : South
C : South
D : South
B cannot reach A/C
A loops towards B/D
Packets continue to be lost
B:1 D=1

## Slide 23: C recomputes Dijkstra
A
B
C
D
100
A's FIB
B : South
C : South
D : South
D's FIB
A : North
B : North
C : North
C's FIB
A : North
B : East
D : East
B's FIB
A : South
C : South
D : South
B loops towards A/C
A can reach everyone
Packets continue to be lost

## Slide 24: D recomputes Dijkstra
A
B
C
D
100
A's FIB
B : South
C : South
D : South
D's FIB
A : West
B : North
C : West
C's FIB
A : North
B : East
D : East
B's FIB
A : South
C : South
D : South
B can reach everyone
A can reach everyone
Network has been updated

## Slide 25: Router failures
Planned failures
  Router reboot to upgrade OS
Sudden failure
  due to power outage, software or hardware crash

## Slide 26: Comparing routing protocols
Neighbour detection
Detecting link failures
Detecting router failures
Link weights
What information is distributed ?
  How often ?
How are forwarding tables built ?

## Slide 27: Agenda
Routing protocols
  Distance Vector routing
  Link state routing
Routing in IP networks
Interdomain routing

## Slide 28: Internet routing
  Exterior Gateway Protocol (EGP)
    Routing of IP packets between domains
      Each domain is considered as a blackbox
Interior Gateway Protocol (IGP)
Routing of IP packets inside each domain
Only knows topology of its domain
Domain1
Domain2
Domain3
Domain4

## Slide 29: Intradomain routing
Goal
  Allow routers to transmit IP packets along the best path towards their destination
    best usually means the shortest path
      Shortest measured in seconds or hops
    sometimes best means the less loaded path
  Alternate routes in case of failures
Behavior
  All routers exchange routing information

## Slide 30: Intradomain routing
Static routing
  Only useful in very small domains
Distance vector routing
  Routing Information Protocol (RIP)
    Still widely used in small domains despite its limitations
Link-state routing
  Open Shortest Path First (OSPF)
    Widely used in enterprise networks
  Intermediate System- Intermediate-System (IS-IS)
    Widely used by ISPs

## Slide 31: Agenda
Routing Protocols
Routing in IP networks
  Routing organization
  RIP and OSPF
Interdomain routing

## Slide 32: RIP
  Distance vector
    default period : 30 seconds (with jitter)
    distance vector is multicasted in UDP message to all RIP routers in local subnets
  Optional extension :
    send distance vector after each change
    but some links flaps...
      send distance vector if routing table changed and did not send another vector within the last 5 seconds
Notes: RFC2453 RIP Version 2. G. Malkin. November 1998
Gary Malkin, RIP : an intra-domain routing protocol, Addison-Wesley, 2002

## Slide 33: RIP : message format
  RIP messages are sent over UDP
    port 520

## Slide 34: RIP : Route Entries

## Slide 35: OSPF
Standard link-state routing protocol for TCP/IP networks (IS-IS in ISP networks)
  Builds upon link-state routing with some extensions
  Hierarchical routing with areas
  Designated routers on subnets
  Equal Cost Multipath

## Slide 36: OSPF
Operation
    HELLO packets to discover neighbors
  Update of routing tables
    Link state packets
      acknowledgements, sequence numbers, age
    periodic transmission/ link changes
  Database description
    Link state Request
      used when a router boots to request link state packets from neighbors
Notes: RFC2328 OSPF Version 2. J. Moy. April 1998.
J. Moy, OSPF: Anatomy of an Internet Routing Protocol, Addison Wesley, 1998

## Slide 37: OSPF details
R
R
R
R
2001:db8:1::A/48
2001:db8:1::B/48
2001:db8:1::C/48
2001:db8:1::D/48
2001:db8:1::C/48
2001:db8:1::B/48
2001:db8:1::A/48
2001:db8:1::D/48

## Slide 38: OSPF details (2)
R
R
R
R
2001:db8:1::A/48
2001:db8:1::B/48
2001:db8:1::C/48
2001:db8:1::D/48
2001:db8:1::C/48
2001:db8:1::B/48
2001:db8:1::A/48
2001:db8:1::D/48
LAN

## Slide 39: OSPF details (3)
  Divide network in areas
  Backbone area : network backbone
    all routers connected to two or more areas belong to the backbone area
  All non-backbone areas must be attached to the backbone area
    at least one router inside each area must be attached to the backbone
OSPF routing must allow any router to send packets to any other router

## Slide 40: OSPF details (4)
D
E
R7
R8
R9
R10
C
D
E
R1
R5
R3
R4
RA
RC
RB
Inside each non-backbone area
Routers exchange link state packets to distribute the topology of the area
Routers do not know the topology of other areas, but each router knows how to reach the backbone area
Stub AREA 1
AREA 2
AREA 0
Inside backbone area
Routers exchange link state packets to distribute the topology of the backbone area
Each router knows how to reach the other areas and distance vectors are used to distribute inter-area routes

## Slide 41
OSPF areas

## Slide 42: Equal Cost Multipath
R1
R2
R4
R5
R6
R3
R7
R8
R9
RD

## Slide 43: Load balancing techniques
Per-packet load balancing
  When a router has several equal cost paths to a destination, it sends packets over the different paths using round-robin
  Advantage : fair distribution
  Drawback: can cause reordering for TCP

## Slide 44: Load balancing techniques
Per-flow load balancing
  Router identifies layer-4 flows
    Hash(IPsrc, IPdest, Portsrc, Portdest)
    Each flow assigned to path based on hash
  Advantage : no reordering
  Drawback: if elephant flows are sent along same path, unfairness
How to ensure that all the packets from a single TCP connection follow the same path to avoid reordering ?

## Slide 45: Agenda
Routing Protocols
Routing in IP networks
Interdomain routing
  Routing policies
  BGP basics

## Slide 46: Interdomain routing
Goals
  Allow to transmit IP packets along the best path towards their destination through several transit domains while considering their routing policies of each domain without knowing their detailed topology
  From an interdomain viewpoint, best path often means cheapest path
    Each domain is free to specify inside its routing policy the domains for which it agrees to provide a transit service and the method it uses to select the best path to reach each destination

## Slide 47: Interdomain links
  Private link
    Usually, a leased line between two routers belonging to the two connected domains
R1
R2
DomainA
DomainB
Notes: For more information on the organization of the Internet, see :
G. Huston, Peerings and settlements, Internet Protocol Journal, Vol. 2, N1 et 2, 1999, http://www.cisco.com/warp/public/759/ipj_Volume2.html
For more information on interconnection points or Internet exchanges, see :
http://www.euro-ix.net/
http://www.ripe.net/ripe/wg/eix/index.html
http://www.ep.net/ep-main.html

## Slide 48: Interconnection exchanges
How to efficiently connect several domains together ?
R1
R2
R3
R4
Physical link
Interdomain link

## Slide 49: An Internet exchange point

## Slide 50: AMS-IX
Largest IX in the world

## Slide 51: AMS-IX

## Slide 52: Routing policies
In theory BGP allows each domain to define its own routing policy...
In practice there are two common policies
  customer-provider peering
    Customer c buys Internet connectivity from provider P
  shared-cost peering
    Domains x and y agree to exchange packets without any payment

## Slide 53: Customer-provider peering
Customer Provider
  Principle
    Customer sends to its provider internal routes and routes learned from its customers
    Provider sends to its customers all known routes
AS2
AS1
AS3
AS4
AS7
$
$
$
$
$
Notes: On link AS7-AS4
AS7 advertises its own routes to AS4
AS4 advertises to AS7 the routes that allow to reach the entire Internet
On link AS4-AS2
AS4 advertises its own routes and the routes belonging to AS7
AS2 advertises the routes that allow to reach the entire Internet

## Slide 54: Question
Each AS advertises one prefix (p1 for AS1,...)
Which prefixes are advertised by AS4 to AS2 ?
Customer Provider
AS2
AS1
AS3
AS4
AS7
$
$
$
$
$
Which prefixes are advertised by AS4 to AS7 ?

## Slide 55: Shared-cost peering
AS2
AS1
AS3
AS4
AS7
$
Customer-provider
$
$
$
$
Shared-cost
  Principle
    PeerX sends to PeerY its internal routes and the routes learned from its own customers
    PeerY sends to PeerX its internal routes and the routes learned from its own customers
Notes: On link AS3-AS4
AS3 advertises its internal routes
AS4 advertises its internal routes and the routes learned from AS7 (its customer)
On link AS1-AS2
AS1 advertises its internal routes and the routes received from AS3 and AS4 (its customers)
AS2 advertises its internal routes and the routes learned from AS74(its customer)

## Slide 56: Customer-provider peering : example
      AS7-AS4 peering link
        AS7 advertises its routes to AS4
        AS4 advertises to AS7 all its routes
      AS4-AS2 peering link
        AS4 advertises its own routes et those of its customers (AS7)
        AS2 advertises to AS2 all known routes
AS2
AS1
AS3
AS4
AS7
$
Customer-provider
$
$
$
$

## Slide 57: Question
AS2
AS1
AS3
AS4
AS7
$
Customer-provider
$
$
$
$
Shared-cost
Each AS advertises one prefix (p1 for AS1,...)
Which prefixes are advertised by AS4 to AS3 ?
Which prefixes are advertised by AS2 to AS1 ?

## Slide 58: Shared cost peerings
AS2
AS1
AS3
AS4
AS7
$
Customer-provider
$
$
$
$
Shared-cost
Each AS advertises one prefix (p1 for AS1,...)
Which prefixes are advertised by AS3 to AS1 ?
Which prefixes are advertised by AS1 to AS2 ?
AS5

## Slide 59: Shared-cost peering : example
    AS3-AS4 peering link
      AS3 advertises its own routes
      AS4 advertises its own routes and those received from its clients (AS7)
    AS1-AS2 peering link
      AS1 advertises its own routes and those received from its clients (AS3 and AS4)
      AS1 advertises its own routes and those received from its clients (AS4)
AS2
AS1
AS3
AS4
AS7
$
Customer-provider
$
$
$
$
Shared-cost

## Slide 60: Routing policies
A domain specifies its routing policy by defining on each BGP router two sets of filters for each peer
  Import filter
    Specifies which routes can be accepted by the router among all the received routes from a given peer
  Export filter
    Specifies which routes can be advertised by the router to a given peer
Notes: RFC 2622 Routing Policy Specification Language (RPSL). C. Alaettinoglu, C.
Villamizar, E. Gerich, D. Kessens, D. Meyer, T. Bates, D. Karrenberg,
M. Terpstra. June 1999.
RFC 2650 Using RPSL in Practice. D. Meyer, J. Schmitz, C. Orange, M.
Prior, C. Alaettinoglu. August 1999.
Internet Routing Registries contain the routing policies of various ISPs, see :
http://www.ripe.net/ripencc/pub-services/whois.html
http://www.arin.net/whois/index.html
http://www.apnic.net/apnic-bin/whois.pl

## Slide 61: Simple example with RPSL
AS2
AS1
AS3
AS4
AS7
$
Customer-provider
$
$
$
$
Shared-cost
Import policy for AS4
Import: from AS3 accept AS3
import: from AS7 accept AS7
import: from AS1 accept ANY
import: from AS2 accept ANY
Export policy for AS4
export: to AS3 announce AS4 AS7
export: to AS7 announce ANY
export: to AS1 announce AS4 AS7
export: to AS2 announce AS4 AS7
Import policy for AS7
Import: from AS4 accept ANY
Export policy for AS4
export: to AS4 announce AS7

## Slide 62: Interdomain paths
AS2
AS1
AS3
AS4
AS7
$
Customer-provider
$
$
$
$
Shared-cost
Each AS advertises one prefix (p1 for AS1,...)
Which path will be used from AS7 to AS2 ?
Which path will be used from AS3 to AS2 ?

## Slide 63: Agenda
Routing in IP networks
Interdomain routing
  Routing policies
  eBGP basics
  BGP convergence

## Slide 64: Border Gateway Protocol
  Path vector protocol
    BGP router advertises its best route to each destination
AS2
AS1
AS4
2001:db8:1/48
AS5
prefix:2001:db8:1/48
ASPath: AS1
prefix: 2001:db8:1/48
ASPath: AS4:AS1
prefix: 2001:db8:1/48 ASPath: ::AS2:AS4:AS1
prefix: 2001:db8:1/48 ASPath: AS1
  ... with incremental updates

## Slide 65: BGP : Principles
Principles
  BGP relies on the incremental exchange of path vectors
BGP session established over TCP connection between peers
Each peer sends all its active routes
As long as the BGP session remains up
Incrementally update BGP routing tables
AS3
AS4
R1
R2
BGP
session
BGP Msgs

## Slide 66: BGP basics
2 types of BGP messages
  UPDATE (path vector)
    advertises a route towards one prefix
      Destination address/prefix
      Interdomain path (AS-Path)
      Nexthop
  WITHDRAW
    a previously announced route is not reachable anymore
      Unreachable destination address/prefix

## Slide 67: BGP router
BGP Loc-RIB
Peer[1]
Peer[N]
Import filter
Attribute
manipulation
Peer[1]
Peer[N]
Export filter
Attribute
manipulation
BGP Routing Information Base
Contains all the acceptable routes learned from all Peers + internal routes
BGP decision process selects the best route towards each destination
BGP Msgs from Peer[1]
BGP Msgs from Peer[N]
BGP Msgs to Peer[N]
BGP Msgs to Peer[1]
Import filter(Peer[i])
Determines which BGM Msgs are acceptable from Peer[i]
Export filter(Peer[i])
Determines which routes can be sent to Peer[i]
One best
route to each
destination
All
acceptable routes
BGP Decision Process
BGP Adj-RIB-In
BGP Adj-RIB-Out

## Slide 68: Example
R2
AS20
AS30
R1
R3
AS10
2001:db8:12/48
BGP
R4
AS40
BGP
BGP
UPDATE
prefix: 2001:db8:12/48,
NextHop:R1
ASPath: AS10
UPDATE
prefix: 2001:db8:12/48,
NextHop:R1
ASPath: AS10
UPDATE
prefix: 2001:db8:12/48,
NextHop:R4
ASPath: AS40:AS10
UPDATE
prefix: 2001:db8:12/48,
NextHop:R2
ASPath: AS20:AS10
  What happens if link AS10-AS20 goes down ?
  What happens if link AS10-AS40 goes down ?
Notes: If link AS10-AS20 goes down, AS20 will not consider anymore the path learned from AS10. It will thus remove this path from its routing table and will instead select the path learned from AS40. This will force AS20 to send the following UPDATE to AS30 :

## Slide 69: How to prefer some routes over others ?
R1
RA
RB
Backup: 2Mbps
Primary: 34Mbps
AS1
AS2

## Slide 70: How to prefer some routes over others
Limitations
RA
R1
R2
R3
RB
Cheap
Expensive
AS1
AS2
AS3
AS4
R5
AS5

## Slide 71: BGP router
BGP RIB
Peer[1]
Peer[N]
Import filter
Attribute
manipulation
Peer[1]
Peer[N]
Export filter
Attribute
manipulation
BGP Msgs from Peer[1]
BGP Msgs from Peer[N]
BGP Msgs to Peer[N]
BGP Msgs to Peer[1]
One best
route to each
destination
All
acceptable routes
BGP Decision Process
Import filter
Selection of acceptable routes
Addition of local-pref attribute inside received BGP Msg
Normal quality route : local-pref=100
Better than normal route :local-pref=200
Worse than normal route :local-pref=50
Simplified BGP Decision Process
Select routes with highest local-pref
If there are several routes, choose routes with the shortest ASPath
If there are still several routes tie-breaking rule

## Slide 72: BGP session
Session establishment
def initialize_BGP_session( RemoteAS, RemoteIP):
# Initialize and start BGP session
# Send BGP OPEN Message to RemoteIP on port 179
# Follow BGP state machine
# advertise local routes and routes learned from peers*/
for d in BGPLocRIB :
B=build_BGP_Update(d)
S=Apply_Export_Filter(RemoteAS,B)
if (S != None) :
send_Update(S,RemoteAS,RemoteIP)
# entire RIB has been sent
# new Updates will be sent to reflect local or distant
# changes in routers
Why ?

## Slide 73: Simple export filter
def apply_export_filter(RemoteAS, BGPMsg) :
# check if RemoteAS already received route
if RemoteAS is BGPMsg.ASPath :
BGPMsg=None
# Many additional export policies can be configured :
# Accept or refuse the BGPMsg
# Modify selected attributes inside BGPMsg
return BGPMsg
Why ?

## Slide 74: Simple import filter
def apply_import_filter(RemoteAS, BGPMsg):
if MysAS in BGPMsg.ASPath :
BGPMsg=None
# Many additional import policies can be configured :
# Accept or refuse the BGPMsg
# Modify selected attributes inside BGPMsg
return BGPMsg

## Slide 75: Processing UPDATE
def Recvd_BGPMsg(Msg, RemoteAS) :
B=apply_import_filer(Msg,RemoteAS)
if (B== None): # Msg not acceptable
return
if IsUPDATE(Msg):
Old_Route=BestRoute(Msg.prefix)
Insert_in_RIB(Msg)
Run_Decision_Process(RIB)
if (BestRoute(Msg.prefix) != Old_Route) :
# best route changed
B=build_BGP_Message(Msg.prefix);
S=apply_export_filter(RemoteAS,B);
if (S!=None) : # announce best route
send_UPDATE(S,RemoteAS,RemoteIP);
else if (Old_Route != None) :
send_WITHDRAW(Msg.prefix,RemoteAS, RemoteIP)

## Slide 76: Processing WITHDRAW
else : # Msg is WITHDRAW
Old_Route=BestRoute(Msg.prefix)
Remove_from_RIB(Msg)
Run_Decision_Process(RIB)
if (Best_Route(Msg.prefix) !=Old_Route):
# best route changed
B=build_BGP_Message(Msg.prefix)
S=apply_export_filter(RemoteAS,B)
if (S != None) : # still one best route towards Msg.prefix
send_UPDATE(S,RemoteAS, RemoteIP);
else if(Old_Route != None) : # No best route anymore
send_WITHDRAW(Msg.prefix,RemoteAS,RemoteIP);

## Slide 77: Simple example
AS1 announces one prefix, p
No routing policies
AS1
AS2
AS3
AS4
AS5
How many routes in AS5?
How many routes in AS4?
Notes: Due to the utilization of the local-pref attribute, some paths on the Internet are longer than their optimum length, see :
Lixin Gao and Feng Wang , The Extent of AS Path Inflation by Routing Policies, GlobalInternet 2002

## Slide 78: Simple example
AS1 announces one prefix, p
No routing policies
AS1
AS2
AS3
AS4
p AS1
p AS2:AS1
p AS3:AS2:AS1
p AS1
RIB
p AS3:AS2:AS1
p AS1 (best)
p AS4:AS1
RIB
p AS2:AS1 (best)
p AS4:AS1
Notes: Due to the utilization of the local-pref attribute, some paths on the Internet are longer than their optimum length, see :
Lixin Gao and Feng Wang , The Extent of AS Path Inflation by Routing Policies, GlobalInternet 2002

## Slide 79: Another example
AS1 announces one prefix, p
No routing policies
Links are activated in the following order
  AS1-AS2, AS3-AS4, AS2-AS3, AS1-AS3
AS1
AS2
AS3
AS4
p AS1
p AS2:AS1
p AS3:AS2:AS1
What will AS3 do when receiving this update ?
p AS1
Notes: Due to the utilization of the local-pref attribute, some paths on the Internet are longer than their optimum length, see :
Lixin Gao and Feng Wang , The Extent of AS Path Inflation by Routing Policies, GlobalInternet 2002

## Slide 80: How to prefer routes ?
R1
RA
RB
Backup: 2Mbps
Primary: 34Mbps
AS1
AS2
RPSL-like policy for AS1
aut-num: AS1
import: from AS2 RA at R1 set localpref=100;
from AS2 RB at R1 set localpref=200;
accept ANY
export: to AS2 RA at R1 announce AS1
to AS2 RB at R1 announce AS1
RPSL-like policy for AS2
aut-num: AS2
import: from AS1 R1 at RA set localpref=100;
from AS1 R1 at RB set localpref=200;
accept AS1
export: to AS1 R1 at RA announce ANY
to AS2 R1 at RB announce ANY
Notes: Note that in RPSL, the set localpref construct does not exist. It is replaced with action preference=x. Unfortunately, in RPSL the routes with the lowest preference are preferred. RPSL uses thus the opposite of local-pref....

## Slide 81: How to prefer routes ?
RA
R1
R2
R3
RB
Cheap
Expensive
AS1
AS2
AS3
AS4
R5
AS5
RPSL policy for AS1
aut-num: AS1
import: from AS2 RA at R1 set localpref=100;
from AS4 R2 at R1 set localpref=200;
accept ANY
export: to AS2 RA at R1 announce AS1
to AS4 R2 at R1 announce AS1
    AS1 will prefer to send over cheap link
    But the flow of the packets destined to AS1 will depend on the routing policy of the other domains

## Slide 82: Agenda
Routing in IP networks
Interdomain routing
  Routing policies
  eBGP basics
  BGP convergence

## Slide 83: Limitations of local-pref
  In theory
    Each domain is free to define its order of preference for the routes learned from external peers
    How to reach 2001:db8:1/48 from AS3 and AS4 ?
AS1
AS3
AS4
Preferred paths for AS4
1. AS3:AS1
2. AS1
Preferred paths for AS3
1. AS4:AS1
2. AS1
2001:db8:1/48

## Slide 84
AS1 sends its UPDATE messages ...
AS1
AS3
AS4
2001:db8:1/48
Preferred paths for AS3
1. AS4:AS1
2. AS1
UPDATE
P: 2001:db8:1/48
ASPath: AS1
Routing table for AS3
2001:db8:1/48 ASPath: AS1 (best)
Preferred paths for AS4
1. AS3:AS1
2. AS1
UPDATE
P: 2001:db8:1/48
ASPath: AS1
Routing table for AS4
2001:db8:1/48 ASPath: AS1 (best)
Limitations of local-pref

## Slide 85
First possibility
  AS3 sends its UPDATE first...
AS1
AS3
AS4
Preferred paths for AS3
1. AS4:AS1
2. AS1
2001:db8:1/48
Routing table for AS3
2001:db8:1/48 ASPath: AS1 (best)
UPDATE
P: 2001:db8:1/48
ASPath: AS3:AS1
Preferred paths for AS4
1. AS3:AS1
2. AS1
Routing table for AS4
2001:db8:1/48 ASPath: AS1
2001:db8:1/48 ASPath:AS3:AS1 (best)
    Stable route assignment
Limitations of local-pref

## Slide 86
  AS4 sends its UPDATE first...
AS1
AS3
AS4
2001:db8:1/48
Preferred paths for AS4
1. AS3:AS1
2. AS1
Routing table for AS4
2001:db8:1/48 ASPath: AS1 (best)
Preferred paths for AS3
1. AS4:AS1
2. AS1
UPDATE
Prefix: 2001:db8:1/48
ASPath: AS4:AS1
Routing table for AS3
2001:db8:1/48 ASPath: AS1
2001:db8:1/48 ASPath: AS4:AS1 (best)
    Another (but different) stable route assignment
Limitations of local-pref

## Slide 87
  AS3 and AS4 send their UPDATE together...
AS1
AS3
AS4
Preferred paths for AS3
1. AS4:AS1
2. AS1
2001:db8:1/48
UPDATE
P: 2001:db8:1/48
ASPath: AS3:AS1
Preferred paths for AS4
1. AS3:AS1
2. AS1
UPDATE
P: 2001:db8:1/48 ASPath: AS4:AS1
    AS3 prefers indirect path -> withdraw
    AS4 prefers indirect path -> withdraw
Limitations of local-pref

## Slide 88
  AS3 and AS4 send their UPDATE together...
AS1
AS3
AS4
Preferred paths for AS3
1. AS4:AS1
2. AS1
2001:db8:1/48
Preferred paths for AS4
1. AS3:AS1
2. AS1
WITHDRAW
P: 2001:db8:1/48
    AS3 : indirect route is not available anymore
      AS3 will reannounce its direct route...
WITHDRAW
P: 2001:db8:1/48
    AS4 : indirect route is not available anymore
      AS4 will reannounce its direct route...
Limitations of local-pref

## Slide 89: More limitations local pref
Unfortunately, interdomain routing may not converge at all in some cases...
    How to reach a destination inside AS0 in this case ?
AS1
AS3
AS4
Preferred paths for AS3
1. AS4:AS0
2. other paths
AS0
Preferred paths for AS4
1. AS1:AS0
2. other paths
Preferred paths for AS1
1. AS3:AS0
2. other paths
Notes: In practice, the exchange of BGP UPDATE messages will cease due to the utilization of timers by BGP routers and the routing will stabilize on one of the two stable route assignments.

## Slide 90: Simple example
AS1
AS2
AS3
$
Customer-provider
Shared-cost
$
AS1 announces one prefix, p
Notes: Due to the utilization of the local-pref attribute, some paths on the Internet are longer than their optimum length, see :
Lixin Gao and Feng Wang , The Extent of AS Path Inflation by Routing Policies, GlobalInternet 2002

## Slide 91: Simple example
AS1 announces one prefix, p
AS1
AS2
AS3
AS5
$
Customer-provider
Shared-cost
$
$
AS4
$
Notes: Due to the utilization of the local-pref attribute, some paths on the Internet are longer than their optimum length, see :
Lixin Gao and Feng Wang , The Extent of AS Path Inflation by Routing Policies, GlobalInternet 2002

## Slide 92: Simple example
AS1 announces one prefix, p
  AS1-AS2 or AS2-AS4 fails
AS1
AS2
AS3
AS5
$
Customer-provider
Shared-cost
$
$
AS4
$
$
Notes: Due to the utilization of the local-pref attribute, some paths on the Internet are longer than their optimum length, see :
Lixin Gao and Feng Wang , The Extent of AS Path Inflation by Routing Policies, GlobalInternet 2002

## Slide 93: Simple example
AS1 announces one prefix, p
  AS3-AS4 is initially down and then comes up
AS1
AS2
AS3
$
Customer-provider
Shared-cost
$
$
AS4
$
Notes: Due to the utilization of the local-pref attribute, some paths on the Internet are longer than their optimum length, see :
Lixin Gao and Feng Wang , The Extent of AS Path Inflation by Routing Policies, GlobalInternet 2002

## Slide 94: local-pref and economic relations
In practice, local-pref is often combined with filters to enforce economical relationships
AS1
Prov1
Prov2
Peer1
Peer2
Peer3
Peer4
Cust1
Cust2
$
Customer-provider
$
Shared-cost
$
$
$
Local-pref values used by AS1
> 1000 for the routes received from a Customer
500 – 999 for the routes learned from a Peer
< 500 for the routes learned from a Provider
Notes: This local-pref settings corresponds to the economical relationships between the various ASes.
Since AS1 is paid to carry packets towards Cust1 and Cust2, it will select a route towards those networks whenever possible.
Since AS1 does not need to pay to carry packets towards Peer1-4, AS1 will select a route towards those networks whenever possible.
AS1 will only utilize the routes receive from its providers when there is no other choice.
It is shown in the following papers that this way of utilizing the local-pref attribute leads to stable BGP routes :
Lixin Gao, Timothy G. Griffin, and Jennifer Rexford, "Inherently safe backup
routing with BGP," Proc. IEEE INFOCOM, April 2001
Lixin Gao and Jennifer Rexford, "Stable Internet routing without global
coordination," IEEE/ACM Transactions on Networking, December 2001, pp.
681-692
The RPSL policy of AS1 could be as follows :
RPSL policy for AS1
aut-num: AS1
import: from Cust1 action set localpref=200; accept Cust1
from Cust2 action set localpref=200; accept Cust2
from Peer1 action set localpref=150; accept Peer1
from Peer2 action set localpref=160; accept Peer2
from Peer3 action set localpref=170; accept Peer3
from Peer4 action set localpref=180; accept Peer4
from Prov1 action set localpref=100; accept ANY
from Prov2 action set localpref=100; accept ANY

## Slide 95: local-pref
Which route will be used by AS1 to reach AS5 ?
  and how will AS5 reach AS1 ?
AS1
AS4
AS2
AS3
AS5
$
Customer-provider
Shared-cost
$
$
$
$
$
AS8
$
AS6
AS7
$
$
Internet paths are often asymmetrical
Notes: Due to the utilization of the local-pref attribute, some paths on the Internet are longer than their optimum length, see :
Lixin Gao and Feng Wang , The Extent of AS Path Inflation by Routing Policies, GlobalInternet 2002

## Slide 96: Internet 1990s
  NSFNet
    American backbone
    AUP : no commercial traffic
  Some regional networks
    US regions
    national networks in Europe
  Universities/research labs
    connected to regional networks or directly to NSFNet

## Slide 97: Internet early 2000s
  Tier-1 ISPs
    Dozen transit ISPs shared-cost
    Uunet, Level3, OTIP, ...
  Tier-2 ISPs
    Regional/ National ISPs
    Tier-3 ISPs
    Smaller ISPs, Entreprise Networks, Content providers
    Customers of T2 or T1 ISPs
    shared-cost with other T3 ISPs
Notes: See :
L. Subramanian, S. Agarwal, J. Rexford, and RH Katz. Characterizing the Internet hierarchy from multiple vantage points. In IEEE INFOCOM, 2002

## Slide 98: Today’s Internet
  Hyper Giants
    google, microsoft, yahoo, amazon, ...
    google peers 70% ISPs
  Tier-1 ISPs
  Tier-2 ISPs
  Tier-3 ISPs
  Many peerings at IXPs
Craig Labovitz), Scott Iekel-Johnson, Danny McPherson, Jon Oberheide, Farnam Jahanian, Internet Inter-Domain Traffic, SIGCOMM 2010

## Slide 99: Internet size #AS
Source: http://bgp.potaroo.net

## Slide 100: BGP IPv6 routing tables
Source: http://bgp.potaroo.net

## Slide 101: BGP : IPv4 routing tables
Source: http://bgp.potaroo.net

## Slide 102: AS7007 incident

## Slide 103: RIPE RIS
https://stat.ripe.net/widget/looking-glass#w.resource=2001:6a8::/32
https://stat.ripe.net/AS2611#tabId=at-a-glance
https://stat.ripe.net/2001:6A8::/32#tabId=routing

## Slide 104: Youtube and Pakistan
http://www.ripe.net/internet-coordination/news/industry-developments/youtube-hijacking-a-ripe-ncc-ris-case-study